Attachment A

HUD House

10440 18th Ave S.

Seattle, WA  98168

HABITAT SCOPE OF WORK

EXTERIOR:

Replace gutters or secure to fascia trim

Prep and paint exterior trim as needed.

Clean moss off roof

Replace glass in garage window

Repair and paint fence

Repair or replace outdoor shed for furnace

Prune shrubs and mow/edge lawn

Paint garage door

GENERAL:

Replace electrical panel and remove old fuse box

Service gas furnace and determine if the existing needs to be replaced or not.

Provide new smoke detectors throughout

Paint interior throughout

Replace carpet throughout

LIVING ROOM:

Remove popcorn ceilings

Remove carpet

BEDROOMS:

Remove popcorn ceilings

Remove wallpaper

Replace electrical fixtures

Install new baseboards

Install closet doors and shelf

KITCHEN:

Remove and replace kitchen cabinets and countertops

Install new electric appliances

Replace ceiling tile with drywall

Add GFI outlet

Replace vinyl flooring

BATH:

Replace tub surround

Check underlayment for any leak damage

Replace vinyl flooring

Install new toilet, sink and faucet

Install new vanity cabinet

Install new med. cabinet with mirror.

Install new hardware

Replace exhaust fan

Replace light fixture

Add GFI outlet

WORK TO BE PERFORMED BY TRADES

ELECTRICAL:

Check outlets for ground

Replace electrical panel

Remove fuse box

Replace light fixtures in bath, bedrooms and kitchen

Add GFI in bathroom and kitchen

Replace exhaust fan in bathroom and kitchen

PLUMBING:

Check plumbing for kitchen sink

Check reliability/life of gas water heater

Replace kitchen sink

Plumb for dishwasher

Replace toilet

Replace sink and faucets

GAS:

Service gas furnace

Check out gas water heater

CARPET:

Provide and install pad and carpet in Living room, hall and bedrooms