Review of the Soos Creek Water & Sewer District Water Comprehensive Plan

Service Area The Soos Creek Water & Sewer District owns and operates a water system that primarily serves the cities of Renton and Kent as well as unincorporated areas in King County. The District is located in south central King County in the Green River basin. The District's corporate boundary encompasses approximately 9,400 acres (14.6 square miles), the retail water service area encompasses 16 square miles and the future service area encompasses approximately 35 square miles. Most of the developed areas of the District is within the two cities. Single family residential use will continue to predominate, and land use and zoning patterns are not expected to change significantly in the next twenty years. The District’s water system includes seven pressure zones, five pump stations, four reservoirs (15.1 million gallons of storage), 12-pressure reducing stations, two emergency interties, four supply interties with Seattle Public Utilities (SPU), and almost 222 miles of pipe. All of the District's water is purchased from SPU. The surrounding purveyors include the City of Renton to the north and northwest, Cedar River Water & Sewer District to the north and east, Covington Water District and King County Water District No. 111 to the southeast, and the City of Kent to the west and southwest. The District holds three franchises for water service including franchise No. 12859 (expires October 29, 2022), 13583 (expires July 19, 2024), and 14916 (expires May 24, 2029). Water Use Efficiency The District provides water service to approximately 62,898 people with 17,600 customer accounts. Approximately 65 percent of the water is used by single family residences. The number of equivalent residential units in 2011 was 23,400. The average day demand forecast for 2021 is 5.23 million gallons per day (MGD) and for 2031 it is 5.82 MGD. The maximum day demand is projected to be 12.03 MGD and 13.39 MGD for 2021 and 2031 respectively. The District used a peak-day demand factor of 2.3. Water use per equivalent residential unit was 170 gallons per day (gpd) for the preceding six years. The planning level value used for the water demand projection is 180 gpd. The three-year average annual distribution system loss is approximately 8.9 percent. The District has identified $53.1 million in capital projects to be constructed over the next 20 years. One hundred and fourteen projects, representing a total of $19.6 million, are considered short-term (6-year and 10-year) projects. An additional 151 projects, representing $33.5 million, are considered long-term projects to be constructed during the subsequent 10 years. Sources of funding for improvements are rates, general facility charges and developer extension funds. Reclaimed Water and Regional Planning The District recognizes the value of reclaimed water as a means to conserve and extend the useful life of the potable water supply. The District completed the King County Reclaimed Water Checklist. SEPA The District completed a State Environmental Policy Act (SEPA) checklist for the Plan and, as lead agency, issued a determination of non-significance for the issuance of the Plan on May 2, 2012. There were no appeals.

| A review of the specific statutes, rules, codes, and policies to the water system plan is as follows: |
| --- |
|  | A. General water plan, King County Code (KCC) 13.24.010 | Comments/findings |
| (1) | Review is applicable to utilities that obtain or distribute water in unincorporated King County under KCC 13.24. Review is applicable to districts organized under Title 57 RCW. Is there a need to meet the consistency requirements of RCW 43.20.260? | Yes, the District distributes water in unincorporated King County and so review under KCC 13.24 is appropriate. The district is also organized under Title 57 RCW and so the Plan is subject to King County Council approval. The Washington State Department of Health (DOH) needs to determine consistency of the Plan under RCW 43.20.260. |
| (2) | Consistency with King County Comprehensive Plan (KCCP) and development regulations, and policies including KCC 21A.28.040 development standards, provision of adequate supplies for anticipated growth and development. | Yes, the Plan is consistent. |
| (3) | Infrastructure for existing and future service areas based on adopted land use map. | Yes. The District used adopted land use maps for that portion of the service area within unincorporated King County. |
| (4) | Review proposals for modified or expanded service areas based on compliance with utility’s approved plan, and ability to meet duty to serve requirement. | The District’s retail water service area is identified in the Plan. Subsequent agreements with adjacent purveyors have resulted in the current service area. The retail service area is not expected to change in the future. |
| (5) | Sufficient information to demonstrate the ability to provide service consistent with the requirements of all applicable statutes, codes, rules, and regulations. | Yes, the Plan demonstrates an ability to provide service consistent with applicable statutes, codes, and regulations. The District’s water supplies are sufficient to meet projected peak day demand in 2020. |
| (6) | Monitor and review effectiveness of purveyor conservation plans if within area covered by an approved coordinated water system plan (CWSP). | The District’s conservation program meets minimum state requirements. |
|  | B. Consistency requirements: 13.24.060 |  |
| (7) | State and local health requirements. | Yes. |
| (8) | Creation and maintenance of logical service areas. | Yes, the service area is logical. |
| (9) | Elimination or prevention of duplicate facilities. | Yes. |
| (10) | Promotion of most healthful and reliable services to the public. | Yes. Water purveyed by the District complies with public health standards. |
| (11) | Provision of service at a reasonable cost and maximization of use of public facilities. | Yes, the District’s rates for water service are comparable to the rates charged by similar utilities. |
| (12) | KCCP and other pertinent County adopted plans and policies. | Yes, there is consistency between the District’s plan and the KCCP. |
| (13) | Basin wide or multibasin water plans, sewerage plans, or both when approved by the Washington State Department of Ecology (Ecology) or DOH. | No multibasin water plans are applicable. |
| (14) | Applicable state water quality, water conservation, and waste management standards. | Yes, applicable standards are met. Water purchased from SPU is fluoridated and chlorinated. Yes, applicable water quality standards are met. The three-year rolling average distribution system leakage (DSL) is 8.9 percent, which is less than the ten percent requirement established under the Municipal Water Law. |
| (15) | Water Resources Act (RCW 90.54). | The Plan makes no connection with the requirements of RCW 90.54.180 or RCW 90.03.386. The District will maintain its existing conservation (efficiency) program to comply with DOH’s Water Use Efficiency Rule. |
| (16) | Growth Management Act (GMA) (RCW 36.70A). | The District's water service area includes unincorporated urban areas. The District appropriately used King County land use zoning for these areas. |
| (17) | Groundwater management plans. | Not applicable. |
| (18) | Federally approved habitat conservation plans and recovery plans under the Endangered Species Act (ESA). | Not applicable. |
| (19) | Requirements for salmon recovery under Ch. 77.85 RCW, and other plans, including regional water supply or water resource management plans. | Not applicable. |
| (20) | Applicable requirements to evaluate opportunities for the use of reclaimed water under chapter 90.46 RCW and CO-7. | The District evaluated reclaimed water use but does not use reclaimed water. |
|  | COUNTYWIDE PLANNING POLICIES |  |
| (21) | FW-5: Management of resources for multiple beneficial uses, including flood and erosion hazard reduction. | Not applicable. |
| (22) | FW-12(c): Ensure sufficient water supply for growth and fish habitat needs through long-term planning. | Sufficient water supply for projected growth is available. |
| (23) | CA-5, CA-6, and E-434 and policies to protect quantity and quality of groundwater. | Not applicable. |
| (24) | CO-5: Water supply shall be regionally coordinated. | Yes, the District’s water supply is regionally coordinated. |
| (25) | CO-6: Aggressive conservation efforts shall be implemented. | The District’s conservation program meets minimum state requirements. |
|  | KING COUNTY COMPREHENSIVE PLAN POLICIES |  |
| (26) | F-107: Plan for provision of services to rural areas. | Yes, the District adequately provides water to the rural area. |
| (27) | F-108: King County to work with cities and service providers to establish priority areas for public funding of capital facilities. | The capital improvement program (CIP) is adequate and appropriately focused with funding sources identified. |
| (28) | F-201: All facilities and services should be provided in compliance with provisions and requirements of the Endangered Species Act and the Clean Water Act. | Not applicable. |
| (29) | F-209: Support rural levels of development and not facilitate urbanization. | The District is committed to serving the area consistent with land use. |
| (30) | F-210: Capital facility plans and improvement programs for services to unincorporated King County are consistent with the KCCP. | Yes, the CIP is consistent with the KCCP. |
| (31) | F-211: King County helps coordinate development of utility facilities. | Yes, to the extent applicable, King County will do this. |
| (32) | F-221: King County shall initiate a sub-area planning process with any service provider that declares, in its capital facilities plan, an inability to meet service needs within service area. | Not applicable. The District did not identify any inability to meet service needs within its service area. |
| (33) | F-223: If a service deficiency is identified in a service provider's existing service area, King County and the applicable service provider shall remedy the deficiency through a joint planning process addressing capital improvement programs and long-term funding strategies reuse programs. | Not applicable. The District did not identify any inability to meet service needs within its service area. |
| (34) | F-231: King County supports coordination of regional water supply planning, sales of excess water supplies among municipalities in the region, water quality programs and water conservation, reuse and reclaimed water programs. | Yes, the District supports regional water supply coordination. |
| (35) | F-232: Water utilities that obtain water from, or distribute water in unincorporated King County, and water utilities formed as special purpose districts under Title 57 RCW are required to submit water system plans to the county for review and approval and shall describe in their plans how they intend to meet their duty to provide service within their retail service areas. | The District distributes water in unincorporated King County so the plan is subject to review and approval by the King County Council. The District is committed to meeting its duty to serve in its retail service area by direct service. |
| (36) | F-243: Public drinking water system reservoirs and watersheds should be managed primarily to protect drinking water supplies, but allow multiple uses when not jeopardizing water quality; downstream uses including recreation, fish, and agricultural resources. | Not applicable. |
| (37) | F-244: Groundwater supplies should be protected by preventing land uses that may adversely affect quantity or quality. | Not applicable. |
| (38) | F-246: King County supports interties that allow the transfer of water resources among water utilities to meet the projected demands for growth where such interties meet the requirements of RCW 90.03.383 and are also consistent with any applicable locally adopted comprehensive plans, regional water supply plans, adopted groundwater management plans, watershed plans, approved Coordinated Water System Plans, Endangered Species Act (ESA) response requirements and Clean Water Act requirements. | The District has several interties with utilities that are consistent with locally-adopted comprehensive plans for the distribution of water to meet projected growth demands. |
| (39) | F-249: Utilities with more than one thousand service connections required to submit water system plans for approval to King County shall include an evaluation of reclaimed water use opportunities by completing King County’s Water Reclamation Evaluation. | The District has more than 1,000 service connections and completed King County’s Water Reclamation Evaluation Checklist. |
| (40) | F-251: In its review of water system plans, the UTRC shall consider the criteria provided in KCC 13.24.010, 13.24.060, and 13.24.070, and determine the plan’s consistency with the following: a. Applicable provisions of the King County Comprehensive Plan, land use plans, and development regulations adopted under the Growth Management Act; b. Approved or adopted regional water resource plans, such as basin plans, groundwater plans, watershed-based conservation and recovery plans developed under ESA, salmon recovery plans developed under chapter 77.85 RCW, water resource plans developed under chapter 90.54 RCW, watershed plans developed under chapter 90.82 RCW, and a regional water supply plan or water resource management plan; c. The County’s Regional Wastewater Services Plan; and d. Other applicable provisions of countywide plans managed by King County, as specified in UTRC Guidance or checklists. | The UTRC did consider these issues and recommends approval of the Plan. |
| (41) | F-252: In reviewing proposals for modified and expanded service area boundaries for municipal water suppliers, the UTRC shall consider, in addition to Policy F-251: a. Compliance by the water system with its water system comprehensive plan, including water conservation elements; b. Whether it can meet its duty to provide service within its service area, as required under chapter 43.20 RCW; and c. Consistency with the service provisions of any applicable Coordinated Water System Plan, as adopted in KCC 13.28. | The District is not planning to change its service area. |
| (42) | F-253: Consistent with Countywide Planning Policies, public drinking water system surface water reservoirs and their watersheds should be managed primarily for the protection of drinking water, but should allow for multiple uses, including recreation, when such uses do not jeopardize drinking water quality standards. Public watersheds must be managed to protect downstream fish and agriculture resources. | Not applicable. |
| (43) | F-254 Groundwater-based public water supplies should be protected by preventing land uses that may adversely affect groundwater quality or quantity to the extent that the supply might be jeopardized. The county shall protect the quality and quantity of groundwater used as water supplies through implementation of Policies E-493 through E-497 where applicable. | Not applicable. |