Road Services Division

Fourth Quarter 2015 Expenditures for

Emergent Needs and Unanticipated Project Costs Summary Report

Use of Quick Response

| Project No. | Project Name | 2015/16 Adopted | Fourth Qtr Transfer Amount | Prior Qtrs Transfer Amount | Remaining Appropriation |
| --- | --- | --- | --- | --- | --- |
| 1027163 | Quick Response | $7,000,000 | ($98,000) | ($425,302) | $6,476,698 |

Fourth Quarter Transfer:

The table below presents the project(s) to which the Quick Response fourth quarter amount shown above has been transferred.  The project(s) as well as the correlations to the Strategic Plan and project prioritization are discussed in more detail below.

| Project No. | Project Name | Original Budget | Transfer Amount | Final Budget |
| --- | --- | --- | --- | --- |
| 1127699 | Upper Preston SE/SE 97 Slide Repair | $0 | $98,000 | $98,000 |

During heavy rainstorms on November 14, 2015, a portion of the Upper Preston Road SE embankment washed out due to heavy storm activity and surface run-off.  In addition, the storm event triggered extensive longitudinal cracking in the outside travel lane.  The scope of the project is to repair the washout to reestablish the road shoulder and a portion of the outer road embankment, culvert replacement, and drainage ditch cleaning.  The agency prioritized these expenditures over other unprogrammed needs due to the potential of property and personal losses with the road being a two lane limited access arterial that provides sole ingress and egress to numerous private residences.  This project meets the following key goals of the Roads strategic plan:

Goal 1:  Prevent and respond to immediate operational life safety and property

damage hazards.

Goal 3:  Maintain and preserve the existing roadway facilities network.

Use of Emergent Need Funds

| Project No. | Project Name | 2015/16 Adopted Plus Carry Forward | Fourth Qtr Transfer Amount | Prior Qtrs Transfer Amount | Remaining Appropriation |
| --- | --- | --- | --- | --- | --- |
| 1026798 | Emergent Need | $14,505,689 | ($1,223,070) | ($7,695,189) | $5,587,430 |

The table below presents the project(s) to which the Emergent Need third quarter amount shown above has been transferred.  The project(s) as well as the correlations to the strategic plan and project prioritization are discussed in more detail below.

Fourth Quarter Transfers:

| Project No. | Project Name | Original Budget | Transfer Amount | Final Budget |
| --- | --- | --- | --- | --- |
| 1127589 | NE 165th Street Flood Risk Reduction | $110,000 | $650,146 | $760,146 |
| 1127590 | 212th Avenue SE Flood Risk Reduction | $176,000 | $233,594 | $409,594 |
| 1127591 | 185th Avenue NE Flood Risk Reduction | $65,000 | $339,330 | $404,330 |

Emergent Need funds were used to supplement an unanticipated grant awarded by the King County Flood Control District for the above referenced projects.  The projects meet the following key goals of the Roads strategic plan:

Goal 1:  Prevent and respond to immediate operational life safety and property

damage hazards.

Goal 3:  Maintain and preserve the existing roadway facilities network.

Project No. 1127589 - NE 165th Street Flood Risk Reduction

The scope of the project is to raise the road elevation to alleviate routine flooding and closure of this arterial that is a bypass route for the Woodinville Duvall Road.  During rain events, NE 165th Street between 179th Place NE and 183rd Place NE becomes flooded in a low spot in the road – up to three feet deep at times – and is subsequently closed.  The road is frequently closed for most of the winter and spring.  Drivers often chose to move or drive past “road closed” signs, and enforcing the closures has not stopped this activity.

Project No. 1127590 - 212th Avenue SE Flood Rick Reduction

The scope of the project is to install an underground overflow conveyance system to alleviate routine roadway and agricultural area flooding.  During rain events, about 1,100 linear feet of the south bound lane of 212th Avenue SE becomes flooded, and is subsequently closed as a result of clogged ditches and the road’s proximity to the ponded wetland.

Project No. 1127591 - 185th Avenue SE Flood Risk Reduction

The scope of the project is to raise the road elevation to alleviate routine flooding.  This road provides the sole access to approximately 150 homes.  During rain events, 185th Avenue NE becomes flooded due to rising lake level, restricting access to the properties.  Wintertime and rain event flooding here is frequent which impacts school children accessing their bus stop.