| Review of the City of Carnation 2015 Comprehensive Water System Plan |
| --- |
| Service Area The City of Carnation (City) owns and operates a water system located in the eastern part of King County. The City’s water system provides potable water to a nine-square-mile planning area both inside the City limits as well as neighboring unincorporated King County. The City is located within the boundary of the East King County Coordinated Water System Planning Area (CWSP). The only adjacent water purveyor is Ames Lake Water District to the west of the City; however, the Snoqualmie River separates them. Nearby water purveyors include Water District 119 to the north and Fall City to the south. System Description The City maintains a spring and a groundwater well for its primary sources of supply. As of 2015, the City served 819 connections and a population of approximately 2,490. The City expects to exceed 1,000 customers in the next five years. The projected population in the year 2035 is 4,705. The majority of the connections are single-family and multifamily residential (approximately 89 percent), but the system also has commercial, industrial, and institutional connections (approximately 11 percent). The water system consists of approximately twelve miles of water lines and over 400 valves. The water system is split into two hydraulic pressure zones with a storage reservoir at the spring and two reservoirs in the City. The groundwater source is a well at Loutsis Park and serves as a backup water supply. The City’s capital improvement plan recommends improvements totaling approximately $15.5 million in projects to be constructed over the next twenty-year period. The improvements will be financed through a low interest rate loan, connection charges and capital project fees. If revenue or funding does not occur as anticipated, then the City may delay its capital improvement schedule. Reclaimed Water The City does not currently have 1,000 or more connections, so it is not required to evaluate water reuse opportunities. However, the City expects to exceed 1,000 connections during the ten-year planning period, so it is currently evaluating reclamation opportunities. The King County Carnation Wastewater Treatment Plant produces reclaimed water using the effluent produced by the City’s residents and businesses. The recycled water is discharged to the Chinook Bend natural area. The City may also investigate and recommend proposed changes to the City's development and service policies and regulations that would promote reclamation programs and technologies. SEPA The Plan is categorically exempt under Washington Administrative Code 197-11-845(2), from the State Environmental Policy Act since the system has fewer than 1,000 connections. |
|  | A. General, water and sewer plan specific King County Code (KCC) 13.24.010 | Comments/findings |
| (1) | The King County Code is applicable to water utilities that obtain or distribute water in unincorporated areas of King County. | The City distributes water in unincorporated areas of King County so review and approval under the King County Code is applicable. |
| (2) | Water system plans should be submitted every six years or sooner if required by the Washington State Department of Health (DOH). | The City’s last water plan was approved in 2009. The Washington State Department of Health approval is pending upon King County’s approval of the plan. |
| (3) | The infrastructure for existing and future service areas based on adopted land use map. | Yes, the infrastructure for existing and future service area is based on the adopted land use map. |
| (4) | The Plan contains sufficient information to demonstrate the ability to provide services consistent with the requirements of all applicable statutes, codes, rules, and regulations. | The Plan demonstrates that the City has ample water supply to provide service consistent with the requirements of all applicable statutes, codes, rules, and regulations for the near term. The City disagrees with Washington State Department of Ecology’s assessment of the water rights held by the City. The City may have an instantaneous diversion/extraction rate problem in the future if demand exceeds 628 gallons per minute. |
| (5) | The Plan is consistent with Washington Administrative Code (WAC) 246-290-100 for the water service. | Yes, the Plan is consistent with the applicable rules. |
| (6) | King County Code related to the installation of fire hydrants and water mains. | Existing fire flow in portions of the service area outside the City do not meet standards. The Plan proposes near-term capital improvement projects to address the shortfalls. |
| (7) | State and local health requirements. | The Plan has not yet been approved by DOH. The UTRC review process included a representative of Public Health - Seattle and King County. |
| (8) | Elimination or prevention of duplicate facilities. | The City intends to provide direct service within its service area by means of direct connection. There are no municipal purveyors in the vicinity of the planning area. No municipal water purveyor is close enough to intertie with. |
| (9) | Promotion of most healthful and reliable services to the public. | Yes. |
| (10) | Provision of service at a reasonable cost, and maximization of use of public facilities. | Currently, the City charges a rate that is in the affordable range. |
| (11) | Consistency with the King County Comprehensive Plan (KCCP) and applicable County plans and policies including the Flood Hazard Management Plan and Emergency Response Plan. | Yes, the Plan is consistent with the applicable comprehensive plans and policies. |
| (12) | Consistency with the Coordinated Water System Plans (CWSP) adopted in KCC 13.28. | Yes, the Plan is consistent with the East King County CWSP. The City does not expect to expand its service area. |
| (13) | Basin-wide or multi-basin water plans, sewerage plans, or both when approved by the Washington State Department of Ecology or the Washington State Department of Health. | The City acknowledges salmon recovery priorities and the relevance of Endangered Species Act listings. |
| (14) | Applicable state water quality, water conservation (e.g., chapter 90.54 RCW and RCW 90.48.495), and waste management standards. | The City’s water use efficiency report for 2016 states that distribution system loss is 16.2 percent of total water produced. The City’s rolling three-year average distribution system loss is of 19.4 percent of total water produced. With the City’s water loss greater than 10 percent, the code requires the City to develop a water loss control action plan to reduce distribution system loss. The City’s water use efficiency goal is to reduce water consumption by one percent per year over the six-year period beginning in July 2013. In 2015, the City averaged 172 gallons per day per equivalent residential unit. |
| (15) | Growth Management Act; chapter 36.70A RCW. | Yes, the Plan is consistent with the Growth Management Act. See specific policies below. |
| (16) | Groundwater Management Plans. | The City owns one ground water well used as a backup supply and for summer time peaking. |
| (17) | Federally-approved habitat conservation plans and recovery plans under Endangered Species Act, and other plans, including regional water supply or water resource management plans. | The City recognizes that several fish species native to the Puget Sound region in which Carnation is located have been listed as either threatened or endangered under the Endangered Species Act. The City states it will implement those Best Management Practices it deems necessary to prevent, or minimize risk of, an unauthorized “take” of a protected species when maintaining and operating the water system, replacing existing water facilities, and constructing new water facilities. |
| (18) | Applicable requirements to evaluate opportunities for the use of reclaimed water under chapter 90.46 RCW. | The City does not currently have 1,000 or more connections, so it is not required to evaluate water reuse opportunities. The King County Carnation Wastewater Treatment Plant produces reclaimed water using the effluent produced by the City’s residents and businesses. The recycled water is discharged to the Chinook Bend natural area. The City may investigate and recommend proposed changes to the City's development and service policies and regulations that would promote reclamation programs and technologies. |
| (19) | State Environmental Policy Act documentation. | The Plan is categorically exempt under Washington Administrative Code 197-11-845(2), from the State Environmental Policy Act review because the system has fewer than 1,000 connections. |
|  | COUNTYWIDE PLANNING POLICIES |  |
| (20) | DP‐13: All jurisdictions shall plan to accommodate housing and employment targets. This includes: “Coordinating water, sewer, transportation and other infrastructure plans and investments among agencies, including special purpose districts;…”. | Yes, the City does this. |
| (21) | PF‐4: Develop plans for long‐term water provision to support growth and to address the potential impacts of climate change on regional water resources. | The City monitors both its surface and groundwater sources and reports no changes to source water quality over time. The City has ample water rights to meet the projected 20-year demand. The Plan does not discuss climate change impacts on water supply. |
| (22) | PF‐5: Support efforts to ensure that all consumers have access to a safe, reliably maintained, and sustainable drinking water source that meets present and future needs. | Yes, the City does this. |
| (23) | PF‐6: Coordinate water supply among local jurisdictions, tribal governments, and water purveyors to provide reliable and cost‐effective sources of water for all users, including residents, businesses, fire districts, and aquatic species. | The City is in the eastern portion of the East King County CWSP and is not contiguous with any other purveyors. The City has no interties with other systems. |
| (24) | PF‐7: Plan and locate water systems in the Rural Area that are appropriate for rural uses and densities and do not increase the development potential of the Rural Area. | The City is very aware of its service to the rural area and ensures service is consistent with and respects King County’s Comprehensive Plan. |
| (25) | PF‐8: Recognize and support agreements with water purveyors in adjacent cities and counties to promote effective conveyance of water supplies and to secure adequate supplies for emergencies. | Not applicable. |
| (26) | PF‐9: Implement water conservation and efficiency efforts to protect natural resources, reduce environmental impacts, and support a sustainable long‐term water supply to serve the growing population. | The volume of water for distribution system loss exceeds the State standard of ten percent. The City should be developing a water loss control plan. |
| (27) | PF‐10: Encourage water reuse and reclamation, especially for high‐volume non‐potable water users such as parks, schools, and golf courses. | Not applicable as the City identified no high- volume irrigation uses nor need for recycled water. |
|  | KING COUNTY COMPREHENSIVE PLAN (KCCP) POLICIES |  |
| (28) | F-107: Plan for provision of services to rural areas. | Yes, the City does this. |
| (29) | F-108: King County to work with cities and service providers to establish priority areas for public funding of capital facilities. | The City’s capital improvement program has sufficient funding based on its current rate structure. |
| (30) | F-201: All facilities and services should be provided in compliance with provisions and requirements of the Endangered Species Act (ESA) and the Clean Water Act. | Yes, to the extent known, facilities and service are provided consistent with the federal laws. |
| (31) | F-209: Support rural levels of development and not facilitate urbanization. | Yes, the City service to the rural area is consistent with the County’s policy. |
| (32) | F-210: Capital facility plans and improvement programs for services to unincorporated King County are consistent with the KCCP. | The City’s capital facility plan is consistent with the KCCP. |
| (33) | F-211: King County helps coordinate development of utility facilities. | Yes, to the extent applicable, King County will do this. |
| (34) | F-221: King County shall initiate a sub-area planning process with any service provider that declares, in its capital facilities plan, an inability to meet service needs within service area. | Not applicable. The City did not identify any inability to meet service needs within its service area. |
| (35) | F-223: If a service deficiency is identified in a service provider's existing service area, King County and the applicable service provider shall remedy the deficiency through a joint planning process addressing capital improvement programs and long-term funding strategies reuse programs. | Not applicable. The City did not identify any inability to meet service needs within its service area. |
| (36) | F-231: King County supports coordination of regional water supply planning, sales of excess water supplies among municipalities in the region, water quality programs and water conservation, reuse and reclaimed water programs. | Yes, the City supports regional water coordination. |
| (37) | F-232: Water utilities that obtain water from, or distribute water in unincorporated King County, and water utilities formed as special purpose districts under Title 57 RCW are required to submit water system plans to the County for review and approval and shall describe in their plans how they intend to meet their duty to provide service within their retail service areas. | The City distributes water in unincorporated areas of King County so review and approval under the King County Code is applicable. The City did describe service area policies for its retail service area. |
| (38) | F-248 King County shall partner with utilities to publicize water conservation and encourage best management practices that conserve potable water supply through measures that include use of alternative supplies such as reclaimed water. | Yes, the County will do this. |
| (39) | F-246: King County supports interties that allow the transfer of water resources among water utilities to meet the projected demands for growth where such interties meet the requirements of RCW 90.03.383 and are also consistent with any applicable locally adopted comprehensive plans, regional water supply plans, adopted groundwater management plans, watershed plans, approved Coordinated Water System Plans, and response requirements of ESA and Clean Water Act. | The Plan is consistent with the East King County CWSP. The City has no interties with other purveyors. |
| (40) | F-249: Utilities with more than one thousand service connections required to submit water system plans for approval to King County shall include an evaluation of reclaimed water use opportunities by completing King County’s Water Reclamation Evaluation. | The City is not required to complete the King County Water Reclamation Evaluation. The City is considering recycled water opportunities. |
| (41) | F-251: In its review of water system plans, the UTRC shall consider the criteria provided in KCC 13.24.010, 13.24.060, and 13.24.070, and determine the plan’s consistency with the following: a. Applicable provisions of the King County Comprehensive Plan, land use plans, and development regulations adopted under the Growth Management Act; b. Approved or adopted regional water resource plans, such as basin plans, groundwater plans, watershed-based conservation and recovery plans developed under ESA, salmon recovery plans developed under chapter 77.85 RCW, water resource plans developed under chapter 90.54 RCW, watershed plans developed under chapter 90.82 RCW, and a regional water supply plan or water resource management plan; c. The County’s Regional Wastewater Services Plan; and d. Other applicable provisions of countywide plans managed by King County, as specified in UTRC Guidance or checklists. | The UTRC did consider these issues and recommends approval of the Plan. |
| (42) | F-252: In reviewing proposals for modified and expanded service area boundaries for municipal water suppliers, the UTRC shall consider, in addition to Policy F-251: a. Compliance by the water system with its water system comprehensive plan, including water conservation elements; b. Whether it can meet its duty to provide service within its service area, as required under chapter 43.20 RCW; and c. Consistency with the service provisions of any applicable Coordinated Water System Plan, as adopted in King County Code Chapter 13.28. | The City is not planning to change its service area boundaries. |
| (43) | F-253: Consistent with Countywide Planning Policies, public drinking water system surface water reservoirs and their watersheds should be managed primarily for the protection of drinking water, but should allow for multiple uses, including recreation, when such uses do not jeopardize drinking water quality standards. Public watersheds must be managed to protect downstream fish and agriculture resources. | Not applicable. |
| (44) | F-254: Groundwater-based public water supplies should be protected by preventing land uses that may adversely affect groundwater quality or quantity to the extent that the supply might be jeopardized. The County shall protect the quality and quantity of groundwater used as water supplies through implementation of Policies E-493 through E-497 where applicable. | The City owns a groundwater well. The City completed a Wellhead Protection Plan some time ago and proposes to update the Wellhead Protection Plan. |