| Review of the Water District No. 49 Water System Plan February 2019 |
| --- |
| Service Area King County Water District No. 49 (District) is a Group A water system serving an urban area in southwestern King County in the Lake Burien area. The District is bound by King County Water District No. 20 to the north, northwest and east, with King County Water District No. 125 to the east and by Highline Water District to the south and southwest. In addition, the District shares a portion of its southeastern boundary with the Port of Seattle's SeaTac Airport. The District covers approximately 3.32 square miles of mostly developed urban land located largely within the City of Burien with smaller portions located in the Cities of Normandy Park and SeaTac. The District's service area is primarily residential with localized commercial developments, including retail stores, shops, and restaurants. The District's Capital Improvement Plan for conveyance and treatment improvements projects expenditures of $27,476,074 over the next ten-year time-period. Water System The District owns and maintains approximately 59.1 miles of water mains, 640 fire hydrants with related isolation valves, control valves, and a 500,000 above-grade gallon concrete storage reservoir and booster pump station. Some water piping smaller than four-inch diameter is plastic or galvanized iron pipe. Pipes four-inches in diameter and larger are ductile iron or cast iron. The District has no asbestos cement pipe within its service area. As of December 2018, there were approximately 4,209 residential, multi-family and commercial metered service connections to the water system. In most cases, multi-family connections include multiple units fed from one metered connection. As of the end of 2018, 391 multi-family connections served approximately 3,540 individual units. The total population served is estimated at 13,577. The projected population for 2038 is for 16,212 residents. Average day water demand in 2019 is estimated to be 1.35 million gallons a day (mgd). Projected average day demand in 2024 is 1.46 mgd. Reclaimed Water Wastewater generated within the District's service area is treated by the Southwest Suburban Sewer District (SWSSD). Currently, SWSSD does not produce reclaimed water at either of its treatment plants. The District completed the King County Water Reclamation Evaluation as part of the Plan. Opportunities for the use of reclaimed water are limited. SEPA The District completed a State Environmental Policy Act (SEPA) checklist for the Plan and, as lead agency, issued a determination of nonsignificance for the issuance of the Plan on February 1, 2019. There were no appeals. |
| A review of the specific statutes, rules, codes and policies to the water system plan is as follows: |
|  | A. General water plan, King County Code (KCC) 13.24.010 and 13.28 | Comments/findings |
| (1) | Review is applicable to water utilities distributing or obtaining water in unincorporated King County, and/or utilities that are special purpose district created pursuant to Title 57 Revised Code of Washington (RCW). Is there a need to meet the consistency requirements of RCW 43.20.260? | Yes, the King County Water District No. 49's 2019 Water System Plan (Plan) is subject to King County Council approval under Title 57 RCW. Yes, The Washington State Department of Health (DOH) also needs to demonstrate consistency for the Plan under RCW 43.20.260. |
| (2) | Consistency with King County Comprehensive Plan (KCCP) and development regulations, and policies including KCC 21A.28.040 development standards, provision of adequate supplies for anticipated growth and development. | Yes, the District's Plan is consistent. |
| (3) | Infrastructure for existing and future service areas based on adopted land use map. | Yes. The District's service area is located entirely in incorporated areas and appropriately used the cities adopted land use. |
| (4) | Review proposals for modified or expanded service areas based on compliance with utility's approved plan, and ability to meet duty to serve requirement. | Not applicable. The District's service area is well defined, as the District is bounded on all sides by other water utilities. The service area has not changed recently and is not expected to change. |
| (5) | Sufficient information to demonstrate the ability to provide service consistent with the requirements of all applicable statutes, codes, rules, and regulations. | Yes, the Plan demonstrates an ability to provide service consistent with applicable statutes, codes and regulations. The District obtains its water from Seattle Public Utilities (SPU) through its Cedar and Tolt River distribution mains. Average day water demand in 2019 is estimated to be 1.35 million gallons a day (mgd). Projected average day demand in 2024 is 1.46 mgd. The District is current with its required water quality monitoring with no recent exceedances of contaminants. |
| (6) | Monitor and review effectiveness of purveyor conservation plans if within area covered by an approved Coordinated Water System Plan (CWSP). | The District is not in an area covered by a CWSP. The District along with Seattle and other water utilities participate in the Saving Water Partnership. The District's water use efficiency plan is organized to conform to the requirements of the Water Use Efficiency Rule. |
|  | B. Consistency requirements: 13.24.060 |  |
| (7) | State and local health requirements. | Yes, water purveyed meets State and local health requirements. |
| (8) | Creation and maintenance of logical service areas. | Yes, the service area is logical. |
| (9) | Elimination or prevention of duplicate facilities. | Yes. The District intends to provide service within its service area by means of direct connection. The District does not foresee any need to provide satellite management services, since direct service is available throughout its service area. The District has entered into agreements with neighboring water utilities and maintains seven interties with two of the adjacent water districts. The District has five interties with King County Water District No. 20 and two interties with the Highline Water District. |
| (10) | Promotion of most healthful and reliable services to the public. | Yes. The hydraulic analysis of the District's system identifies the need for improvements to storage. The District also identified the need to replace undersized water mains to improve pressure and velocity conditions. The District's contract for water from SPU expires in January 1, 2062. Water purveyed by the District complies with public health standards. |
| (11) | Provision of service at a reasonable cost, and maximization of use of public facilities. | Yes, the District's rates for water service are comparable to the rates charged by similar utilities. The District has adopted a graduated rate structure to encourage efficiency of water use. |
|  | King County Comprehensive Plan and other pertinent county adopted plans and policies. | Yes, there is consistency between the District's Plan and the King County Comprehensive Plan. |
| (12) | Basin-wide or multi-basin water plans, sewerage plans, or both when approved by the Washington State Department of Ecology (Ecology) or Department of Health (DOH). | The District has not been involved in multibasin water plans, although it does take part in SPU initiatives. The District neither collects nor treats wastewater. |
| (13) | Applicable state water quality, water conservation, and waste management standards. | Yes, applicable standards are met. The District receives treated water from SPU which does all the testing. The District does coliform monitoring in keeping with State guidelines. For the ten-year period 2008 through 2017, average usage was 158 gallons per equivalent residential unit (ERU) day. The value of 165 gpd/ERU was selected for projecting future water demand. The District's distribution system loss (non-revenue or unaccounted-for water) for 2018 was 6.1 percent and the three-year average is 3 percent and meets the statutory goal. |
| (14) | Water Resources Act (RCW 90.54). | The Plan makes no connection between the District's conservation program and the requirements of RCWs 90.54.180 and 90.03.386. |
| (15) | Growth Management Act (GMA) (RCW 36.70A). | The District has a conservation program in place. |
| (16) | Groundwater management plans. | Not applicable as the District's source is surface water. |
| (17) | Federally approved habitat conservation plans and recovery plans under the Endangered Species Act (ESA). | Not discussed in Plan. |
| (18) | Requirements for salmon recovery under Ch. 77.85 RCW, and other plans, including regional water supply or water resource management plans. | Not discussed in Plan. |
|  | C: Countywide Planning Policies |  |
| (19) | G-4: Adopt comprehensive plans that are consistent with the Countywide Planning Policies as required by the Growth Management Act. | Yes, the District adopted a plan that is consistent with Countywide Planning Policies. |
| (20) | EN-19: Promote energy efficiency, conservation methods and sustainable energy sources to support climate change reduction goals. | Not discussed in Plan. |
| (21) | DP-13: All jurisdictions shall plan to accommodate housing and employment targets. This includes coordinating water, sewer, transportation and other infrastructure plans and investments among agencies, including special purpose districts. | Yes, the District asserts it can accommodate population and employment targets of the cities within its service area. |
| (22) | PF-2: Coordinate among jurisdictions and service providers to provide reliable and cost-effective services to the public. | Yes, the District has coordinated with neighboring service providers with interties for emergency supply. |
| (23) | PF-4: Develop plans for long‐term water provision to support growth and to address the potential impacts of climate change on regional water resources. | Sufficient water supply for growth is available. Climate change is not mentioned, however the District's source water is from the Seattle system. Seattle has considered climate change and water yield from their source. |
| (24) | PF-7: Plan and locate water systems in the Rural Area that are appropriate for rural uses and densities and do not increase the development potential of the Rural Area. | Not applicable as the District serves an urban area. |
| (25) | PF-8: Recognize and support agreements with water purveyors in adjacent cities and counties to promote effective conveyance of water supplies and to secure adequate supplies for emergencies. | Yes, the District's supply is regionally coordinated, since it purchases its water from SPU under a long-term contract. The District also has agreements with neighboring water systems (King County Water District No. 20 and Highline Water District) for emergency supplies. |
| (26) | PF-9: Implement water conservation and efficiency efforts to protect natural resources, reduce environmental impacts, and support a sustainable long‐term water supply to serve the growing population. | The water conservation and efficiency efforts of the District meet the minimum required by statute. The distribution system loss in 2018 was 6 percent with a three-year rolling average of 3.1 percent. The distribution system loss is within or meets State standards. |
| (27) | PF-10: Encourage water reuse and reclamation, especially for high‐volume non‐potable water users such as parks, schools, and golf courses. | The District evaluated water reclamation opportunities and found use of reclaimed water is not be viable at this time. The Plan includes the King County Water Reclamation Evaluation form in Appendix L. |
|  | D: King County Comprehensive Plan (KCCP) |  |
| (28) | F-107: With special purpose districts or local service providers, plan for provision of services to rural areas. | Not applicable as the District serves in the urban area. |
| (29) | F-108: King County to work with cities and service providers to establish priority areas for public funding of capital facilities. | Yes, King County will do this. |
| (30) | F-201: All facilities and services should be provided in compliance with provisions and requirements of the Endangered Species Act and the Clean Water Act. | The Plan makes no reference to the Endangered Species Act or the Clean Water Act. However, the District's water source is from the SPU system and SPU has a Habitat Conservation Plan for the Cedar River watershed. |
| (31) | F-209: In the Rural Area, services provided by agencies should support a rural level of development and not facilitate urbanization. | Not applicable. |
| (32) | F-210: capital facility plans and capital improvement programs for services to unincorporated King County are consistent with the KCCP. | Not applicable. |
| (33) | F-211: King County helps coordinate development of utility facilities with other projects that utilize public rights-of-way and easements, where possible. | Not applicable. |
| (34) | F-221: King County shall initiate a sub-area planning process with any service provider that declares, in its capital facilities plan, an inability to meet service needs within service area. | Not applicable as the District did not identify an inability to meet service needs within its service area. |
| (35) | F-223: If a service deficiency is identified in a service provider's existing service area, King County and the applicable service provider shall remedy the deficiency through a joint planning process addressing capital improvement programs and long-term funding strategies. | Not applicable as the District did not identify an inability to meet service needs within its service area. |
| (36) | F-231: King County supports coordination of regional water supply planning, sales of excess water supplies among municipalities in the region, water quality programs and water conservation, reuse and reclaimed water programs. | The District has interties with neighboring utilities to provide emergency water supply. |
| (37) | F-232: Water utilities that obtain water from, or distribute water in unincorporated King County, and water utilities formed as special purpose districts under Title 57 RCW are required to submit water system plans to the county for review and approval and shall describe in their plans how they intend to meet their duty to provide service within their retail service area. | The District does not provide water to unincorporated areas. The District is a special purpose district formed under Title 57 RCW. The District can meet its duty to serve in the designated retail service area. |
| (38) | F-246: King County supports interties that allow the transfer of water resources among water utilities to meet the projected demands for growth where such interties meet the requirements of RCW 90.03.383 and are also consistent with any applicable locally adopted comprehensive plans, regional water supply plans, adopted groundwater management plans, watershed plans, approved Coordinated Water System Plans, Endangered Species Act response requirements and Clean Water Act requirements. | The District has an intertie with the neighboring water utilities to provide emergency water supply. |
| (39) | F-249: Utilities with more than one thousand service connections required to submit water system plans for approval to King County shall include an evaluation of reclaimed water use opportunities by completing King County's Water Reclamation Evaluation Checklist. | Yes, the District completed King County's Water Reclamation Evaluation Checklist. |
| (40) | F-251: In its review of water system plans, the UTRC shall consider the criteria provided in K.C.C. 13.24.010, 13.24.060, and 13.24.070, and determine the plan's consistency with the following: a. Applicable provisions of the King County Comprehensive Plan, land use plans, and development regulations adopted under the Growth Management Act; b. Approved or adopted regional water resource plans, such as basin plans, groundwater plans, watershed-based conservation and recovery plans developed under ESA, salmon recovery plans developed under chapter 77.85 RCW, water resource plans developed under chapter 90.54 RCW, watershed plans developed under chapter 90.82 RCW, and a regional water supply plan or water resource management plan; c. The county's Regional Wastewater Services Plan; and d. Other applicable provisions of countywide plans managed by King County, as specified in UTRC guidance or checklists. | The UTRC has reviewed the planning data and the District's operations and has found the Plan is consistent with: a. the King County Comprehensive Plan, land use plans and development regulations; b. to the extent applicable, the basin plans, groundwater plans, watershed-based conservation and recovery plans for the service area; and c. other applicable provisions. |
| (41) | F-252: In reviewing proposals for modified and expanded service area boundaries for municipal water suppliers, the UTRC shall consider, in addition to Policy F-251: a. Compliance by the water system with its water system comprehensive plan, including water conservation elements; b. Whether it can meet its duty to provide service within its service area, as required under chapter 43.20 RCW; and c. Consistency with the service provisions of any applicable Coordinated Water System Plan, as adopted in King County Code Chapter 13.28. | Not applicable as the District is not changing its water service area. |
| (42) | F-253: Consistent with Countywide Planning Policies, public drinking water system surface water reservoirs and their watersheds should be managed primarily for the protection of drinking water, but should allow for multiple uses, including recreation, when such uses do not jeopardize drinking water quality standards. Public watersheds must be managed to protect downstream fish and agriculture resources. | Not applicable as the District does not control any surface water reservoirs or watersheds. |
| (43) | F-254: Groundwater-based public water supplies should be protected by preventing land uses that may adversely affect groundwater quality or quantity to the extent that the supply might be jeopardized. The county shall protect the quality and quantity of groundwater used as water supplies through implementation of Policies E-493 through E-497 where applicable. | Not applicable as the District's source of water is surface water. |