| Review of City of Renton Long-Range Wastewater Management Plan dated July 2022 |
| --- |
| Service Area The City of Renton (City) provides sanitary sewer service to approximately 25.6 square miles both inside and outside the City limits; outside the City limits the service area includes areas of Kent, Tukwila, and unincorporated King County. Overall, the City’s collection system contains approximately 14,000 customer connections. The City’s collection system is municipally owned, operated, and maintained; the system is managed by the City’s Public Works Department. The City’s entire service area is entirely within the King County urban growth area boundary. The City projects the population to increase from 68,286 (2012) to 114,117 (2040) within the service area. The number of employees is projected to increase from 44,506 (2012) to 104,414 (2040). Sewer System The City's collection system consists of approximately 247 miles of gravity mains (1,304,160 feet), over 6,700 manholes, 5.16 miles (27,433 linear feet [LF]) of force mains (FMs), and 20 lift stations that collect and convey wastewater to King County’s regional transmission interceptors. These interceptors convey the City’s flow to the King County owned and operated South Treatment Plant for treatment. The City’s Capital Improvement Plan includes improvements projects totaling $96,590,000 over the next 20 years. The short-term (2020 – 2025) time period projects total $26,970,000; the medium-term (2026 – 2029) time period projects total $17,800,000; and the long-term (2030 – 2039) projects total $52,100,000. Reclaimed Water The City is participating in a working group consisting of King County, Cascade Water Alliance, Seattle Public Utilities, and individual surrounding purveyors, in combined effort to develop a master agreement for reclaimed water as well as reclaimed water planning and policies. The forum represents a regional approach to strategic planning and system expansions needed to accommodate the distribution, sale, supply, and reuse of reclaimed water that could include the City's current and future service area. In 2011, the King County Wastewater Treatment Division began another engineering, environmental, and economic analysis of conceptual reclaimed water strategies. The City is now working with King County to provide it appropriate information for this analysis. The City’s plan states that it will support the regional supplier's study of reclaimed water use opportunities and will work with King County Department of Natural Resources and Parks to identify potential reclaimed water users and demand. The City has identified several potential users of reclaimed water for landscape irrigation uses, including the Boeing Longacres Facilities. SEPA The City completed a State Environmental Policy Act (SEPA) checklist for the Plan and, as lead agency under SEPA, issued a determination of nonsignificance for the approval of the Plan on June 17, 2021. There were no appeals. |
| A review of the specific statutes, rules, codes, and policies to the water system plan is as follows: |
|  | A. General and sewer plan-specific requirements of King County Code (KCC) 13.24.010 | Comments/findings |
| (1) | Review and approval by the King County Council is applicable to public or private entities that provide sewer collection or treatment in unincorporated areas of King County as required by KCC ch. 13.24 | The review and approval the City of Renton’s Long-Range Wastewater Management Plan (Plan) is required as the City collects and conveys wastewater to King County’s Interceptors which flow to the King County owned and operated South Treatment Plant. The City’s sewer service area extends into unincorporated King County. |
| (2) | The Plan shall be consistent with the King County Comprehensive Plan and development regulations and policies. | The Plan acknowledges the unincorporated urban area of the City’s Potential Annexation Area (PAA). The growth projections are consistent with the adopted targets. |
| (3) | The Plan shall be adopted by that entity and approved by the King County Council as a prerequisite for the following: Operating in unincorporated King County; Approval of annexation proposals; Granting of new right-of-way franchises and right-of-way franchise renewals; and Approval of right-of-way construction permits, except for emergency permits issued under KCC 14.44.055. | The City adopted the Plan on September 19, 2022 through Resolution No. 4478 prior to submission to the County for approval. The City’s service area extends into unincorporated King County. The current franchise agreement expires in 2026. |
| (4) | Plans should be submitted every six years or sooner if required by the Washington State Department of Ecology (DOE), or whenever sewer conditions have changed significantly within sewer service area. | The City’s last wastewater plan is dated 2010 and was approved by King County Ordinance 17015 on January 6, 2011. |
| (5) | Infrastructure for existing and future service areas based on adopted land use map. | The growth inputs into the hydraulic model are derived from Puget Sound Regional Council (PSRC) forecasts and are consistent with adopted growth targets. |
| (6) | Sufficient information to demonstrate the ability to provide service consistent with the requirements of all applicable statutes, codes, rules, and regulations. | Future growth is modeled through the existing hydraulic model of the collection system. The model was used as a basis to perform a capacity analysis. Based on the severity of the deficiencies identified, the most probable cause and the location, four types of recommendations were developed to mitigate or confirm these problem areas: 1) additional long‐term depth monitoring, 2) infiltration and inflow (I/I) evaluation, 3) piping reconfiguration, and 4) programmatic upsizing. |
| (7) | Consistent with Washington Administrative Code (WAC) 173-240-050. | The Department of Ecology (DOE) has reviewed the City of Renton's Long Range Wastewater Management Plan dated July 2022 and approved it on November 17, 2022. |
| (8) | Discuss the following: Existing and planned flows, average and peak; Existing and planned flows for any basin discharging into the County system; Amounts of inflow and infiltration (I/I), in comparison with County standard of 1,100 gallons per-acre-per-day (GPAD) and steps being taken to reduce; Areas of concern regarding corrosion and odor control, and steps being taken to address; and Opportunities for reclaimed water. | The Plan includes a discussion of existing and planned flows. A temporary flow monitoring program was conducted to correlate actual collection system flows to the hydraulic model predicted flows, evaluate the system's capacity, and estimate basin Infiltration and Inflow (I/I). The flows referenced in the Plan reflect flows that discharge into the County system. The plan indicates that the acceptable I/I is 1,500 gallons per acre per day (GPAD) as determined between a joint planning effort between King County and component agencies. There are segments of the system that exceed 1,500 GPAD. Reduction in I/I is occurring through the City’s mainline and lateral replacement program. Some segments of the sewer system have reached the end of their useful life. The Plan recommends a program to address condition issues of these aging sanitary sewers through rehabilitation and replacement. The City supports the regional supplier's study of reclaimed water use opportunities and will work with King County Department of Natural Resources and Parks to identify potential reclaimed water users and demand. The City has identified several potential users of reclaimed water for landscape irrigation uses, including the Boeing Longacres Facilities. |
|  | B. Public Sewer Service: KCC 13.24.035 |  |
| (9) | All developments within Urban Growth Area (UGA) served by sewer unless on-site systems are allowed on an interim basis per KCC 13.24.136. | All new development within the Urban Growth Area will be served by public sewers except in situations where a single-family residence on an individual lot would be denied all reasonable use of the property or sewer service is not available for a proposed short subdivision in a timely and reasonable manner. |
| (10) | Required elements of a sewerage general plan, as called for in RCW 36.94.010(3), are included in King County Comprehensive Plan and Technical Appendix. | The Plan has the general location and description of treatment and disposal facilities, trunk and interceptor sewers, pumping stations, monitoring and control facilities, channels, local service areas, and a general description of the collection system to serve the service area. The Plan also contains preliminary engineering in adequate detail to assure technical feasibility and, to the extent known, discusses the methods of distributing the cost and expense of the system and the economic feasibility of plan implementation. |
|  | C. Consistency requirements: KCC 13.24.060 |  |
| (11) | State and local health requirements. | The Plan was reviewed by DOE and approved on November 17, 2022. The Utilities Technical Review Committee (UTRC) review process included a representative of Public Health - Seattle & King County. |
| (12) | Elimination or prevention of duplicate facilities and a reduction of number of entities providing sewer service in King County. | No other entities provide sewer service within the service area. The City has entered into several joint use land service agreements with neighboring districts. |
| (13) | Promotion of most healthful and reliable services to the public. | The Plan’s Operational policies and Capital Improvement Program (CIP) promote healthful and reliable services to the utility’s customers. |
| (14) | Provision of service at a reasonable cost, and maximization of use of public facilities. | Rates for service outside City limits are 1.5 times above the rates for service within the City limits. Seniors and disability citizen discounts are available. |
| (15) | Basin wide or multibasin water plans, sewerage plans, or both when approved by DOE or Washington State Department of Health. | The Plan does not refer to the participation of the City with basin-wide or multibasin water plans or sewerage plans. The City is participating in a working group consisting of King County, Cascade Water Alliance, Seattle Public Utilities, and individual surrounding purveyors, in combined effort to develop a master agreement for reclaimed water as well as reclaimed water planning and policies. |
| (16) | Applicable state water quality, water conservation (e.g., RCW 90.48.495), and waste management standards. | Provisions for treatment, discharge, and reuse are not included in the City’s Plan. The King County Service Agreement states that King County will provide all service to Renton and it is the responsibility of King County to receive all flows. |
| (17) | Growth Management Act (GMA), chapter 36.70A RCW. | The Plan conforms to the GMA. Please refer to policy consistency below. |
| (18) | Groundwater Management Plans. | The Plan makes no reference to Groundwater Management Plans. |
| (19) | Federally-approved habitat conservation plans and recovery plans under Endangered Species Act. | The Plan makes no reference to habitat conservation plans and recovery plans. |
| (20) | Requirements for salmon recovery under RCW ch. 77.85, and other plans, including regional water supply or water resource management plans. | The Plan makes no reference to the salmon recovery efforts within the watershed. |
| (21) | Applicable requirements to evaluate opportunities for the use of reclaimed water under chapter 90.46 RCW. | The City supports the regional supplier's study of reclaimed water use opportunities and will work with King County Department of Natural Resources and Parks to identify potential reclaimed water users and demand. The City has identified several potential users of reclaimed water for landscape irrigation uses, including the Boeing Longacres Facilities. |
| (22) | State Environmental Policy Act documentation. | The City completed a State Environmental Policy Act (SEPA) checklist for the Plan and, as lead agency under SEPA, issued a determination of nonsignificance for the approval of the Plan on June 17, 2021. There were no appeals. |
|  | COUNTYWIDE PLANNING POLICIES |  |
| (23) | FW-4: Support fiscal sustainability for infrastructure and services that serve rural areas. | The wastewater service area does not extend into the rural area of unincorporated King County. |
| (24) | PF-11: Require water reuse and reclamation where feasible. | See #8 above. |
| (25) | DP-3 and PF-3: Coordination of capital facilities and service plans to promote efficient land use and reliable and cost-effective services. | The review by the UTRC and approval by the County Council promotes coordination of capital facilities and service plans. |
| (26) | DP- 14: Adopted infrastructure plans are consistent with adopted growth targets. | The growth projections are consistent with the adopted targets. |
| (27) | DP-49, PF-1 and PF-13: Limit the extension of urban infrastructure improvements through the Rural Area. | The wastewater service area includes existing cities’ boundaries and its Potential Annexation Areas within the unincorporated Urban Growth Area. |
| (28) | PF-12: With few exceptions, require development with the UGA to be served by public sewer. | See #9 above. |
|  | KING COUNTY COMPREHENSIVE PLAN POLICIES |  |
| (29) | F-101 and F04: Forging partnerships in identifying appropriate service providers and coordinate planning efforts. | The review and adoption of the Sewer Plan demonstrates partnership and coordination efforts. |
| (30) | F-107 and F-209: Plan for provision of services to rural areas. | The sewer service area does not expand into the designated rural area. |
| (31) | F-201 and F-210: Water and sewer utilities that provide services to unincorporated King County shall prepare capital facility plans consistent with requirements of the GMA and King County Comprehensive Plan. | The Long-Range Wastewater Management Plan is consistent with the GMA and King County Comprehensive Plan as it limits service to within the designated urban area and incorporates future growth projections consistent with King County’s adopted growth targets. |
| (32) | F-255: All development within UGA to be served by public sewers, with few exceptions. | See #9 above. |
| (33) | F-256: King County and sewer utilities should jointly plan for phasing out of on-site systems within UGA. | A customer policy objective is to “Actively promote connection to the public sewers by all residents within the City’s service area. “ |