| Review of Lakehaven Utility District Comprehensive Wastewater Plan, 2009 |
| --- |
|  | A. General and sewer plan-specific requirements of King County Code 13.24.010 | Comments/findings |
| (1) | Review and approval by the King County Council is applicable to: special purpose districts under Revised Code of Washington (RCW) 57.16.010(6); and sewer districts that provide sewer collection or treatment in unincorporated areas of King County. Review of the plan is also required under King County Code (KCC) 28.84 as the District is a component agency of the regional system. | The review and approval of the Comprehensive Wastewater Plan, 2009 (Plan) is required as the Lakehaven Utility District (District) is a special purpose district authorized by and operated under Title 57 RCW. A portion of the District’s service area lies within unincorporated King County as well as within the Cities of Federal Way, Des Moines, Kent, Auburn, Pacific, Edgewood, Milton, Tacoma and unincorporated Pierce County. A portion of the District’s wastewater flows are treated by the regional system. |
| (2) | The Plan shall be consistent with the King County Comprehensive Plan and development regulations and policies. | Yes. See below for details. For the King County Comprehensive Plan the applicable policies are listed along with the policy or operational activity the District takes related to the policy. |
| (3) | The Plan shall be adopted by that entity and approved by the King County Council as a prerequisite for the following: Operating in unincorporated King County; Approval of annexation proposals; Granting of new right-of-way franchises and right-of-way franchise renewals; and Approval of right-of-way construction permits, except for emergency permits issued under KCC 14.44.055. | Based on the previously approved Plan(s) the County has granted two franchises to the District. Franchises held by the District are numbers 12379 and 15141 and there is no need to amend either of them at this time. The District covers a significant portion of southwest unincorporated King County within the urban growth area. The East Federal Way Potential Annexation Area is within the District’s service area. |
| (4) | Plans should be submitted every six years or sooner if required by the Washington State Department of Ecology (DOE), or whenever sewer conditions have changed significantly within sewer service area. | The District’s last wastewater plan is dated 1999 and was approved by King County in March 2002, Ordinance 14303. |
| (5) | Infrastructure for existing and future service areas based on adopted land use map. | Yes, for that portion of the service area in unincorporated King County, the County’s zoning was used. For the potential annexation area of the City of Federal Way, the City’s proposed zoning was used. |

| (6) | Sufficient information to demonstrate the ability to provide service consistent with the requirements of all applicable statutes, codes, rules, and regulations. | Yes. See below for details as to existing facilities and plans for improvements. The District used a system hydraulic model to evaluate its collection capacity, and concluded that there is adequate capacity to accommodate peak flows and anticipated growth to the year 2030 for that portion of the District that discharges to the regional system. |
| --- | --- | --- |
| (7) | Consistent with Washington Administrative Code (WAC) 173-240-050. | Yes. DOE has reviewed the Plan and provided comments to the District. DOE will only approve the Plan when it is consistent with WAC 173-240 and RCW 90.48.110. |
| (8) | Discuss the following: Existing and planned flows, average and peak; Existing and planned flows for any basin discharging into County system; Amounts of inflow and infiltration (I/I), in comparison with County standard of 1,100 gallons/acre/day (gpad) and steps being taken to reduce; Areas of concern regarding corrosion and odor control, and steps being taken; and Opportunities for reclaimed water. | The existing and planned for flows were developed with a standard method and are reasonable for those flows discharged to the County’s system. The 20-year storm event peak I/I for the year 2000 was modeled to be 2,600 gpad. This is over our 1,100 gpad threshold but not extremely excessive. These flows are not on their own contributing to any capacity shortfalls in that part of the District’s system contributing to the regional system. There were no issues identified with either corrosion or odor control. Independent of this Plan, the District evaluated opportunities for use of reclaimed water within and near the District and documented the assessment in a study, “Water Reclamation Related Engineering Services Feasibility Study.” |
|  | B. Public Sewer Service: 13.24.035 |  |
| (9) | All developments within Urban Growth Area (UGA) served by sewer unless on-site are allowed as temporary per KCC 13.24.136 and 13.08.070. | Yes, the District understands its service area is entirely within the UGA and anticipates providing sewer service within its entire service area for new development. There are estimated to be as many as 6,500 existing on-site disposal systems within the corporate area, and they cover approximately 20 percent of the District’s service area. The District is planning to serve those users if and when the on-site systems fail. The District is supportive of property owner initiated utility local improvement districts; however, there is no proactive program to convert existing on-site systems to the regional system. The District anticipates the residential population served will grow from 114,000 in 2008 to approximately 140,000 by 2030. |
| (10) | Required elements of sewerage general plan, as called for in RCW 36.94.010(3), are included in King County Comprehensive Plan and Technical Appendix. | The Plan has the general location and description of treatment and disposal facilities, trunk and interceptor sewers, pumping stations, monitoring and control facilities, channels, local service areas, and a general description of the collection system to serve the service area. The Plan also contains preliminary engineering in adequate detail to assure technical feasibility and, to the extent known, discusses the methods of distributing the cost and expense of the system and the economic feasibility of plan implementation. |
|  | C. Consistency requirements: 13.24.060 |  |
| (11) | State and local health requirements. | The Plan has been reviewed and approved by DOE, with responses to DOE’s comments incorporated into the revised Plan. The Utilities Technical Review Committee review process included a representative of Public Health Seattle and King County. |
| (12) | Elimination or prevention of duplicate facilities and a reduction of number of entities providing sewer service in King County. | The District has written agreements with local general purpose governments and other sewer providers as to areas to be served in order to avoid overlapping jurisdiction. No other entities provide sewer service within the service area. |
| (13) | Promotion of most healthful and reliable services to the public. | Yes. |
| (14) | Provision of service at a reasonable cost, and maximization of use of public facilities. | Sewer rates appear reasonable. |
| (15) | Basin wide or multibasin water plans, sewerage plans, or both when approved by DOE or Washington State Department of Health. | The District is aware of, and supports, the planning done in the Green River basin for salmon recovery purposes. The District is part of the regional wastewater system managed by King County. |
| (16) | Applicable state water quality, water conservation (e.g., RCW 90.48.495), and waste management standards. | Yes, the two treatment plants operated by the District meet their permit requirements. There is no indication in the Plan as to whether the District’s planned water conservation efforts would reduce flows into its sewerage system or have any impact on its conveyance capacity. |

| (17) | Growth Management Act (GMA), chapter 36.70A RCW. | Yes, the Plan is consistent with the King County Comprehensive Plan and development regulations used to implement the GMA. |
| --- | --- | --- |
| (18) | Groundwater Management Plans. | Groundwater quality will be protected if the District implements a septic abandonment program to connect areas served by on-site septic systems to the regional sewer system. Those actions should reduce public health risk from failing septic systems to underlying aquifers. One possible future use of reclaimed water is for aquifer recharge. |
| (19) | Federally-approved habitat conservation plans and recovery plans under Endangered Species Act (ESA). | The District recognizes its responsibility to avoid take of an endangered species in its operations to treat and dispose of wastewater. |
| (20) | Requirements for salmon recovery under RCW 77.85, and other plans, including regional water supply or water resource management plans. | The Plan makes no reference to the participation of the District with salmon recovery efforts within the watershed. No regional water supply plan is applicable. |
| (21) | Applicable requirements to evaluate opportunities for the use of reclaimed water under chapter 90.46 RCW. | Separate from the development of this Plan, the District conducted an evaluation of the potential use of reclaimed water. The District supports ongoing assessments of potential reclaimed water use but has not found it cost effective at this time. The two most likely future uses are irrigation and groundwater recharge. |
| (22) | State Environmental Policy Act documentation. | Determination of Nonsignificance issued by the District on July 22, 2009, with no appeals. |
|  | COUNTYWIDE PLANNING POLICIES |  |
| (23) | CA-5 and CA-6: adopt policies to protect quantity and quality of groundwater. | Connection of houses and businesses with on-site septic to the District’s sewer system should reduce health risks from any failing septic systems. |
| (24) | CO-7: water reuse and reclamation shall be encouraged, especially for high water users. | See number 21 above. |
|  | KING COUNTY COMPREHENSIVE PLAN POLICIES |  |
| (25) | F-104: plan for provision of services to rural areas. | No rural areas within the District. |
| (26) | E-105: protect critical habitat. | Yes. The District plans to upgrade facilities and address possible I/I problems. This should reduce discharges and assist in improving the water quality of the Puget Sound. |

| (27) | E-434: management and protection of water resources by King County through incentives, regulations and programs. | The District does protect water resource quality through a well run system. |
| --- | --- | --- |
| (28) | E-466: protect groundwater and develop strategies to compensate or mitigate for losses. | See above discussion regarding I/I and sewer service to currently unsewered properties. |
| (29) | E-477: protect and enhance surface waters, including Puget Sound. | See above. |
| (30) | F-105: work with cities and service providers to provide services. | Yes, the District provides service within eight cities and two counties. The District has a long-term goal of treating as much of the wastewater generated within its service areas as possible. In response to that policy, the County noted for the Meredith sub-basin, it is the County’s expectation that wastewater will flow to the regional system indefinitely. The County’s policy or position is detailed in the Regional Wastewater Services Plan. King County ordinance 15757 also provides that the County must exercise its authority under RCW 35.58.200(i) to require certain entities to discharge sewage into the regional system after 2036 as long as there are outstanding sewer revenue bonds. The City of Pacific and King County have an agreement regarding future wastewater flows from the East Hylebos sub-basin that also impacts the District’s policy of treating the maximum amount of wastewater flows generated in the service area. |
| (31) | F-202: ensure adequate supply of public facilities to support communities. | Yes. The District used information from the most recent comprehensive plans of the jurisdictions it overlays. |
| (32) | F-203: work with cities, special purpose utilities, and other service providers to define regional and local services and determine appropriate providers. | Yes, King County has worked with the District to define the service area. The District has written agreements with most of the local governments regarding service provisions. The District needs to continue working with the City of Pacific to define the service areas served by the District and City. |
| (33) | F-207: funding for growth should support facilities needed within UGAs, prioritized and coordinated through capital improvement programs (CIP), to comply with concurrency requirements. | Funding sources are identified to support identified needs, including facilities to serve anticipated population growth under local comprehensive plans. Developer extension agreements are anticipated to be the major source of funding for system expansion. |
| (34) | F-208: support rural levels of development and not facilitate urbanization. | There are no rural areas within the District. |
| (35) | F-210: coordinate development of utility facilities. | Yes. |
| (36) | F-212: King County’s CIP demonstrates that projected needs for facilities and services can be met within the UGA in compliance with concurrency requirements; where not possible, identify strategies including phasing and financing. | Yes. The District’s CIP identifies facilities and a funding strategy to ensure that it will meet anticipated demands. |
| (37) | F-213: water and sewer utilities that provide services to unincorporated King County shall prepare capital facility plans consistent with requirements of GMA and King County Comprehensive Plan. | Yes, the Plan is consistent with the King County Comprehensive Plan and GMA. |
| (38) | F-215 and F-217: where an area wide sewer, water, or transportation deficiency is identified, King County and applicable service providers shall remedy the deficiency through a joint planning process. | Not applicable as no deficiency was identified. |
| (39) | F-245: all development within UGA to be served by public sewers, with some exceptions. | Yes, the policy is being implemented. |
| (40) | F-246: King County and sewer utilities should jointly plan for phasing out of on-site systems within UGA. | The District anticipates its entire service area being served by sewers but recognizes the existing 6,500 on-site systems will be operating for some time. |
| (41) | F-252: King County should monitor failing on-site systems and analyze options which may include connecting to sewerage systems where consistent with the King County Comprehensive Plan. | The District does have a large number (6,500) of existing on-site systems within its service area. There is not a significant number of failing on-site systems within the District’s service area of unincorporated King County. |