Review of the Sammamish Plateau Water and Sewer District 2013 Wastewater Comprehensive Plan

Service Area The Sammamish Plateau Water and Sewer District (District) is located in central King County approximately 15 miles east of the City of Seattle along the Interstate 90 corridor, north of the City of Issaquah. The District is bordered by Lake Sammamish to the west and the Snoqualmie River Valley to the east. The District is generally bounded by the City of Issaquah to the south, Northeast Sammamish Sewer and Water District to the North, Lake Sammamish to the west and unincorporated rural King County to the east. The District is located on terrain characterized by rolling upland hills with crests ranging in elevation from 350 to 620 feet and the lowlands along the southerly and westerly service boundaries near Lake Sammamish ranging in elevations of 30 to 75 feet. The service area is approximately 20 square miles. The District’s future sewer service boundary on the north and east is largely limited by the Urban Growth Boundary, in general terms the sewer service area is bounded by SR 202 on the north and east and I-90 on the south. The area is primarily single-family residential. The service area is not expected to significantly change in the future. The wastewater system currently serves a population of approximately 37,347 people through approximately 13,000 service connections. The District’s gravity wastewater collection and transmission system is comprised of approximately 150 miles of pipe varying in size from 8-inch collectors to 36-inch interceptors, and is relatively new with approximately 90 percent of the system having been constructed since 1980. The District’s wastewater is treated at the South Treatment Plant facility operated by King County. The District’s pipes extend along SE 56th Street (as NW Sammamish Road), eventually connecting into the King County sewer system at Manhole R17-36, near the entrance to Lake Sammamish State Park. The Plan contains a capital improvement plan with an estimated cost of $21,558,000 for sewer capital projects within the next six years and a 20-year estimated cost of $104,716,000 in sewer capital projects for the near and distant future. The District identified funding sources for the proposed improvement projects which include rates, general facilities charges and bond proceeds. Historically, the District’s Franchise 6301 was for the sewer service area. That franchise was incorporated into Franchise 6311 which expired in 2010. The District is working to update the franchise for the sewer service area with Real Estate Services. Reclaimed Water The District does not receive or use reclaimed water but is willing to work with King County to identify opportunities. The District completed the King County Reclaimed Water Checklist. SEPA The District completed a State Environmental Policy Act (SEPA) checklist for the Plan and acting as Lead Agency issued a Determination of Nonsignificance for plan on April 1, 2014. There were no appeals.

|  | A. General, water and sewer plan specific King County Code (KCC) 13.24.010 | Comments/findings |
| --- | --- | --- |
| (1) | The code is applicable to sewer utilities that provide sewer collection or treatment in unincorporated areas of King County and/or are component agencies of the regional wastewater system. | A portion of the District’s service area lies within unincorporated King County. The District is a component agency of the regional conveyance and treatment system and so review and approval of the plan is pursuant to KCC 28.84.050. The District is also subject to Title 57 and approval by the County Council is required by code. |
| (2) | Plans should be submitted every six years or sooner if required by the Washington State Department of Ecology (DOE) whenever sewer conditions have changed significantly within the sewer service area. | The District’s last wastewater plan was approved by King County in 2005. The District will seek wastewater plan approval from the Washington State Department of Ecology |
| (3) | The Plan must meet criteria in chapter 90.48 Revised Code of Washington (RCW) as well as KCC as follows: (1) compliance with the development program and policies outlined in the King County Comprehensive Plan for sewage facilities; and (2) compliance with the basin-wide water and/or sewerage plan. . | Yes, the plan meets the criteria in chapter 90.48 RCW and is compliant with the development program in the King County Comprehensive Plan and the basin-wide sewerage plan. |
| (4) | The infrastructure for existing and future service areas based on adopted land use map. | Yes, appropriate land use and zoning for the City of Sammamish, the City of Issaquah and unincorporated King County was used in determining future wastewater flow projections. |
| (5) | The Plan contains sufficient information to demonstrate the ability to provide services consistent with the requirements of all applicable statutes, codes, rules, and regulations. | Yes, the Plan demonstrates that the District has ample wastewater capacity to provide service consistent with the requirements of all applicable statutes, codes, rules, and regulations. |
| (6) | The Plan is consistent with Washington Administrative Code (WAC) 173-240-050. | Yes, the District will seek plan approval from the DOE. |
| (7) | The Plan discusses the following: Existing and planned flows average and peak; Existing and planned flows for any basin discharging into county system; Amounts of inflow and infiltration (I/I), in comparison with county standard of 1,100 gallons per-acre-per-day (gpad), and steps being taken to reduce; Areas of concern regarding corrosion and odor control and steps being taken; Opportunities for reclaimed water; and Additional information required by the Utilities Technical Review Committee (UTRC). | All are discussed in the Plan: 1, 2, & 3. The existing and planned flow of 155 gallons per day per equivalent residential unit is reasonable. The District worked with the Wastewater Treatment Division of the Department of Natural Resources and Parks on the regional I/I control program. I/I modeling was done at 536 gpad for today and 1,100 gpad at full build out. 4. There were no issues identified with either corrosion or odor control. 5. The District supports King County’s planning efforts regarding reclaimed water opportunities. 6. In its review of the Plan, the UTRC asked for additional information, which has been provided by the District either in the final Plan or in direct communication with the UTRC. |
|  | B. Public Sewer Service: 13.24.035 |  |
| (8) | The Plan proposes that all developments within Urban Growth Area served by sewer unless on-site are allowed as temporary per KCC 13.24.136 and 13.08.070. | There are unserved areas within the District’s sewer service area and the District has a program to extend service to those areas. |
| (9) | Public sewer is provided in rural towns if approved by King County. | There are no rural towns in the District’s sewer service area. |
| (10) | No public sewer service outside Urban Growth Area unless authorized under KCC 13.24.134. | All of the District’s sewer service area is within the Urban Growth Area. Sewer service is consistent with KCC 13.24.035. The District acknowledges that sewer service beyond the Urban Growth Area would be consistent with KCC 13.24.134. |
| (11) | Required elements of sewerage general plan, as called for in RCW 36.94.010(3), are included in King County Comprehensive Plan and Technical Appendix. | Yes, the Plan has the general location and description of treatment and disposal facilities, trunk and interceptor sewers, pumping stations, monitoring and control facilities, local service areas, and preliminary engineering in adequate detail to assure technical feasibility and, to the extent known, the methods of distributing the cost and expense of the system and the economic feasibility of plan implementation. |
|  | C. Consistency requirements: 13.24.060 |  |
| (12) | State and local health requirements. | The Plan has not yet been reviewed and/or approved by the DOE. The UTRC review process included a representative of Public Health-Seattle and King County. |
| (13) | Elimination or prevention of duplicate facilities. | The District has written agreements with other sewer providers regarding areas to be served in order to avoid overlapping jurisdiction and to ensure efficiency in the use of existing facilities. |
| (14) | Promotion of most healthful and reliable services to the public. | Yes. |
| (15) | Provision of service at a reasonable cost, and maximization of use of public facilities. | Currently the District charges a rate that is in the affordable range. In general, the District collects revenues in excess of expenditures. |
| (16) | Reduction of number of entities providing sewer service in King County. | The District has written agreements with other sewer providers regarding areas to be served in order to avoid overlapping jurisdiction and to ensure efficiency in the use of existing facilities. |
| (17) | Basin wide or multibasin water plans, sewerage plans, or both when approved by the Washington State Department of Ecology or the Washington State Department of Health. | The District is part of the regional wastewater system managed by King County. |
| (18) | Applicable state water quality, water conservation (e.g., RCW 90.48.495), and waste management standards. | Yes. As the District implements water conservation programs, there may be a minimal impact on the operation of the sewer system. |
| (19) | Growth Management Act (GMA); chapter 36.70A RCW. | Yes, the Plan is consistent with the King County Comprehensive Plan and GMA. |
| (20) | Groundwater Management Plans. | The Plan does reference groundwater protection as one of the goals of the sewer plan. |
| (21) | Federally-approved habitat conservation plans and recovery plans under Endangered Species Act, and other plans, including regional water supply or water resource management plans. | The District is aware of, and supports, the planning done for salmon recovery purposes. There is no applicable regional water supply plan. |
| (22) | Applicable requirements to evaluate opportunities for the use of reclaimed water under chapter 90.46 RCW. | Yes, the District supports King County’s planning efforts. The District completed the King County Reclaimed Water Checklist. |
| (23) | Sewer facilities allowed crossing rural areas only under certain conditions and only for schools or public health emergencies, under certain conditions. KCC 13.24.132. | The District understands and complies with the King County Code. |
| (24) | State Environmental Policy Act documentation. | Determination of Nonsignificance issued by the County on April 1, 2014, with no appeals. |
|  | COUNTYWIDE PLANNING POLICIES |  |
| (25) | PF‐1 Provide a full range of urban services in the Urban Growth Area to support the Regional Growth Strategy and adopted growth targets and limit the availability of services in the Rural Area consistent with VISION 2040. | Yes, the District does this. |
| (26) | PF‐2 Coordinate among jurisdictions and service providers to provide reliable and cost effective services to the public. | Yes, the District has in place interlocal agreements or contracts to provide reliable and cost effective services to the public. |
| (27) | PF‐10: Encourage water reuse and reclamation, especially for high‐volume non‐potable water users such as parks, schools, and golf courses. | The District may continue to work with King County to identify opportunities and explore ownership and management options to produce and deliver reclaimed water. |
| (28) | PF‐11: Require all development in the Urban Growth Area to be served by a public sewer system with minor exceptions. | Yes, the District is committed to serving the Urban Growth Area. |
| (29) | PF‐12: Prohibit sewer service in the Rural Area and on Resource Lands except: a) where needed to address specific health and safety problems threatening existing structures; or b) as allowed by Countywide Planning Policy DP‐47; or c) as provided in Appendix 5 (March 31, 2012 School Siting Task Force Report). | Yes, the District’s plan demonstrates that service to the rural area will only be done consistent with King County Code. |
|  | KING COUNTY COMPREHENSIVE PLAN POLICIES |  |
| (30) | F-107: plan for provision of services to rural areas. | The District’s service area abuts the rural area. The District’s plan acknowledges that sewer service to the rural area will be done consistent with the King County Code. |
| (31) | E- 408 King County should carry out conservation planning efforts in close collaboration with other local governments, tribes, state and federal governments, land owners, and other conservation planning stakeholders. | Yes. |
| (32) | E-422: King County’s land use planning, regulatory, and operational functions related to environmental protection, public safety, and equity should be closely coordinated across departments and with other applicable agencies and organizations to achieve an ecosystem-based approach. | Not applicable. |
| (33) | E-434: Habitats for species that have been identified as endangered, threatened, or sensitive by the state or federal government shall not be reduced and should be conserved. | Yes, the District operates the system to protect habitat. |
| (34) | F-108 work with cities and service providers to provide services. | Yes, the District has agreements with neighboring service providers to ensure coordinated service. |
| (35) | F-201 All facilities and services should be provided in compliance with provisions and requirements of the Endangered Species Act and the Clean Water Act. | Yes, the District does this. |
| (36) | F-202: ensure adequate supply of public facilities to support communities. | Yes. The District included review and incorporation of information from the most recent King County Comprehensive Plan in the Plan. |
| (37) | F-204: work with cities, special purpose utilities, and other service providers to define regional and local services and determine appropriate providers. | Yes. The District has written agreements with local governments and special purpose utilities regarding service provision and coordination with other systems. |
| (38) | F-208: funding for growth should support facilities needed within Urban Growth Areas, prioritized and coordinated through capital improvement programs (CIP), to comply with concurrency requirements. | Funding sources are identified to support identified needs, including facilities to serve anticipated population growth under local comprehensive plans. Extension of the sewer system will be primarily by developer extension agreements. |
| (39) | F-209: support rural levels of development and not facilitate urbanization. | Yes. |
| (40) | F-211: coordinate development of utility facilities. | Yes, see 34. |
| (41) | F-212: King County’s CIP demonstrates that projected needs for facilities and services can be met within the Urban Growth Area in compliance with concurrency requirements; where not possible, identify strategies including phasing and financing. | Yes. The District’s CIP identifies facilities and a funding strategy to ensure that it will meet anticipated demands. |
| (42) | F-214: water and sewer utilities that provide their services to unincorporated King County, shall prepare capital facility plans consistent with requirements of the Growth Management Act and King County Code. | Yes. |
| (43) | F-221: King County shall initiate a subarea planning process with any service provider that declares, through their capital facilities plan, an inability to accommodate projected service needs inside their service area. | Not applicable as the District has the ability to accommodate projected service needs in the service area. |
| (44) | F-223: if an area wide sewer, water, or transportation deficiency is identified, King County and applicable service providers shall remedy the deficiency through a joint planning process. | Not applicable. |
| (45) | F-255: in the Urban Growth Area, all new development shall be served by public sewers with minor exceptions. | Yes, the District is prepared to serve the urban area. |
| (46) | F- 256: in the Urban Growth Area, King County and sewer utilities should jointly prioritize the replacement of onsite systems that serve existing development with public sewers, based on the risk of potential failure. King County and sewer utilities should analyze public funding options for such conversion and should prepare conversion plans that will enable quick and cost-effective local response to health and pollution problems that may occur when many on-site systems fail in an area. | Yes, the District has policies in place to ensure and encourage the use of the sanitary sewer system within the urban area. Extension of the sewer system will be primarily by developer extension agreements. The District estimates that approximately 3,486 on-site systems exist within its sewer service area and has policies in place to phase out their use over time. |
| (47) | F-259: sewer facilities such as pump stations, force mains and trunk lines that do not provide connections to the Rural Area may be located in the Rural Area only when they are identified in a King County-approved comprehensive sewage system plan and upon a finding by King County that it is technically necessary in providing service to the Urban Growth Area. | Yes, the District understands and abides by this policy. |
| (48) | F-260: on-site facilities in rural and natural resource areas shall be designed, constructed, and operated as permanent facilities. | Not applicable. |
| (49) | F- 261: King County should monitor failing on-site systems and analyze options which may include connecting to sewerage systems where consistent with the King County Comprehensive Plan. | There is no significant number of failing on-site systems within the District’s service area of unincorporated King County. |
| (50) | F-262: collective on-site systems may only be used in rural and natural resource areas under specified conditions. | Not applicable. |