| Sammamish Plateau Water & Sewer District Wastewater Comprehensive Plan Update and General Sewer Plan (February 2023) |
| --- |
| Service Area The Sammamish Plateau Water and Sewer District (District) is in east King County, between Lake Sammamish (to the west) and the Snoqualmie River Valley (to the east). The District is located 15 miles east of the City of Seattle and includes portions of the cities of Sammamish and Issaquah and areas of unincorporated King County. The sewer service area can be generally described as the urban zoned areas east of Lake Sammamish, north and east of I-90, and south and west of SR 202; it excludes the Issaquah Highlands area and the northeast section of the City of Sammamish. The District boundary encompasses approximately 29 square miles. The District’s future sewer service area covers approximately 20 square miles. The District’s sewer customers are predominantly single-family residential, accounting for approximately 89 percent of the current sewer service connections. As of the end of 2020, the District had 13,077 sewer connections (17,075 ERUs) providing service to approximately 50,800 people. While the District’s sewer service population is estimated to grow to 77,185 people by 2040, this growth includes the transition from septic systems within the urban area to sewer service, in addition to new connections associated with new development. Currently, approximately 3,390 on-site septic systems are present within the District’s sewer service area; most properties served by these septic systems are in an area to which the sewer system has not yet been extended. With only two exceptions for schools, sewer service is only provided to urban areas within the urban growth boundary. Sewer System The District has agreements with King County as the regional wastewater purveyor. The District’s sewer collection system flows into and is treated by the King County Wastewater Treatment Division (KCWTD) sewer system. Currently, all flows are directed to the South Treatment Plant in Renton via the Southern Diversion. Plans include a second connection to the King County system to the north via the North Diversion. The District maintains and services approximately 159 miles of gravity sewer main, 10 miles of low-pressure force main, 21 lift stations, approximately 15 miles of force main, 563 grinder pumps, and a supervisory control and data acquisition (SCADA) system. Reclaimed Water The Plan references a Cascade Water Alliance Transmission and Supply Plan (TSP) that was originally approved in 2012 and extended in 2019 as providing the reclaimed water elements for inclusion in the District’s Comprehensive Water System Plan. The TSP plan identified five potential “small source” reclaimed water use sites within the District’s service area. These include irrigation use at two schools, two parks, and one apartment complex. The District’s Plan includes an implementation service strategy to continue consideration of water reuse opportunities. SEPA The District completed a State Environmental Policy Act (SEPA) checklist for the Plan and, as lead agency under SEPA, issued a determination of nonsignificance for the approval of the Plan on September 21, 2022. There were no appeals. |
| A review of the specific statutes, rules, codes, and policies to the water system plan is as follows: |
| King County Code/Policies | Comments/findings |
| A. General and sewer plan-specific requirements of King County Code (KCC) 13.24.010 |
| (1) | Review and approval by the King County Council is applicable to public or private entities that provide sewer collection or treatment in unincorporated areas of King County as required by KCC ch. 13.24 | The District’s sewer service area extends into unincorporated King County. The District’s wastewater is conveyed to a King County treatment facility. |
| (2) | The Plan shall be consistent with the King County Comprehensive Plan and development regulations and policies. | The Plan acknowledges the unincorporated King County zoning classifications. This information is used to develop maximum zoning capacity population estimates. The Plan acknowledges and includes policies that support King County policies and regulations pertaining to sewer service. |
| (3) | The Plan shall be adopted by that entity and approved by the King County Council as a prerequisite for the following: Operating in unincorporated King County; Approval of annexation proposals; Granting of new right-of-way franchises and right-of-way franchise renewals; and Approval of right-of-way construction permits, except for emergency permits issued under KCC 14.44.055. | The District Board of Commissioners adopted the Plan on March 6, 2023, through Resolution No. 5182 prior to submission to the County for approval. The District’s service area does extend into unincorporated King County and conveys waste to a King County treatment plant. |
| (4) | Plans should be submitted every six years or sooner if required by the Washington State Department of Ecology (DOE), or whenever sewer conditions have changed significantly within sewer service area. | The District's last wastewater plan was completed in 2014 and approved in 2015 by King County Ordinance 18061. |
| (5) | Infrastructure for existing and future service areas based on adopted land use map. | The Plan acknowledges the unincorporated King County zoning classifications. This information is used to develop buildout capacity estimates. Growth rates in the Plan are compiled from: (1) currently proposed developments; (2) Sammamish Town Center assumptions; and (3) conversion of existing homes from septic to sewer service. The infrastructure plan for the service area assumes some properties currently served by onsite septic will be connected to sewer system within the planning horizon. |
| (6) | Sufficient information to demonstrate the ability to provide service consistent with the requirements of all applicable statutes, codes, rules, and regulations. | The District conducted an evaluation of its existing system to identify system deficiencies and necessary improvements and to project system expansion requirements. An updated hydraulic model was used in addition to asset management tools and an operational conditions assessment to identify and provide improvements for system deficiencies. The Plan evaluated the reliability of the existing sewer system facilities which includes backup power at lift stations, surcharging capacities, and lift station sequencing and operations. |
| (7) | Consistent with Washington Administrative Code (WAC) 173-240-050. | DOE approved the Plan on April 27, 2023. |
| (8) | Discuss the following: Existing and planned flows, average and peak; Existing and planned flows for any basin discharging into the County system; Amounts of inflow and infiltration (I/I), in comparison with County standard of 1,100 gallons per-acre-per-day (gpad) and steps being taken to reduce; Areas of concern regarding corrosion and odor control, and steps being taken; and Opportunities for reclaimed water. | The current I/I rate averages 570 gpad across all the basins. The highest maximum daily I/I rate measured for the District is 1,947 gpad at the Benham Ridge lift station. This lift station’s basin area is the smallest of the District’s lift stations. The relatively small service area and the relatively small number of residential customer equivalents (RCEs) served results in a low total estimated I/I flow (gpd) despite the relatively high I/I rate on a per-acre basis. I/I rate at zoning capacity averages 1,293 gpad across all the basins. The District visually inspects critical manholes annually and others every 3 years for corrosion. Generator battery terminals are checked monthly for corrosion. The District has conducted smoke testing to identify potential contributors to I/I. Through this effort the District identified illicit connections to the sewer system, some of which were considered significant contributors to inflow into the sewer system. The District is currently working with property owners to eliminate these connections. Most of the odor complaints within the District are associated with the discharge from force mains of lift stations that currently have odor control and include the following: Trossachs, North Lake, Central Lake, and Mallard Bay Lift Stations. The Plan references a Cascade Water Alliance Transmission and Supply Plan (TSP) that was originally approved in 2012 and extended in 2019 as providing the reclaimed water elements for inclusion in the District’s Comprehensive Water System Plan. The TSP plan identified five potential “small source” reclaimed water use sites within the District’s service area. These include irrigation use at two schools, two parks, and one apartment complex. The District’s Plan includes an implementation service strategy to continue consideration of water reuse opportunities. The District has concerns over introduction of reclaimed water into the environment, as per- and poly-fluoroalkyl substances (PFAS) have been detected in effluent from both King County Treatment Plants and reclaimed water. |
| B. Public Sewer Service: KCC 13.24.035 |
| (9) | All developments within UGA served by sewer unless on-site systems are temporarily allowed per KCC 13.24.136 and 13.08.070. | The District requires properties in the urban area that are developing or properties responding to a failing onsite septic system, or other situations that require modification to an onsite septic system, to either connect to the sewer system or to sign an Agreement for Future Connection to Sewer. The District will require the installation of dry sewers when an urban property is subdividing or developing using a septic system and the location and design of the sewer can be readily ascertained, without the possibility of constraining the future design of up- or downstream sewer facilities. The Plan includes an implementation policy addressing the development of policies and funding mechanisms to support extension of sewer-to-service to areas currently using septic systems. The District will also enforce conversion of septic to sewer systems when required by a land use jurisdiction or specific property agreement. |
| (10) | Required elements of a sewerage general plan, as called for in RCW 36.94.010(3), are included in King County Comprehensive Plan and Technical Appendix. | The District’s sewer collection system flows into and is treated by the KCWTD sewer system. The Plan has the general location and description of treatment and disposal facilities, trunk and interceptor sewers, pumping stations, monitoring and control facilities, channels, local service areas, and a general description of the collection system to serve the service area. The Plan also contains preliminary engineering in adequate detail to assure technical feasibility and, to the extent known, discusses the methods of distributing the cost and expense of the system and the economic feasibility of plan implementation. |
| C. Consistency requirements: KCC 13.24.060 |
| (11) | State and local health requirements. | The Plan was reviewed and approved by DOE on April 27, 2023. The Utilities Technical Review Committee (UTRC) included a representative of Public Health - Seattle & King County. |
| (12) | Elimination or prevention of duplicate facilities and a reduction of number of entities providing sewer service in King County. | The District does have existing agreements, provided in Plan appendix, with adjacent service providers for coordination of service. The Plan does include an implementing policy that requires specific agreements to clarify the extent and conditions for service to be provided to properties outside of the District’s sewer service area. |
| (13) | Promotion of most healthful and reliable services to the public. | The Plan’s Operational Policies and Capital Improvement Plan promotes healthful and reliable services to the utility’s customers. |
| (14) | Provision of service at a reasonable cost, and maximization of use of public facilities. | The Plan references three different affordability metrics in determining if current and future rates would be affordable. It appears the rates are relatively affordable for customers within the District. The District offers a utility bill assistance program that reduces utility bills for qualifying customers. |
| (15) | Basin wide or multibasin water plans, sewerage plans, or both when approved by DOE or Washington State Department of Health. | The Plan does not refer to participation with basin-wide or multi-basin water plans or sewerage plans. |
| (16) | Applicable state water quality, water conservation (e.g., RCW 90.48.495), and waste management standards. | Provisions for treatment, discharge, and reuse are not included in the District’s Plan. The District is not permitted for either wastewater treatment or land application of wastewater. The District sewer collection system flows into and is treated by the KCWTD sewer system. The King County Service Agreement states that King County will provide all service to the District and it is the responsibility of King County to receive all flows. |
| (17) | Growth Management Act (GMA), chapter 36.70A RCW. | The Plan conforms to the GMA. Please refer to policy consistency below. |
| (18) | Groundwater Management Plans. | The Plan makes no reference to Groundwater Management Plans. |
| (19) | Federally-approved habitat conservation plans and recovery plans under Endangered Species Act. | The Plan makes no reference to habitat conservation plans and recovery plans. |
| (20) | Requirements for salmon recovery under RCW 77.85, and other plans, including regional water supply or water resource management plans. | The Plan makes no reference to the salmon recovery efforts within the watershed. |
| (21) | Applicable requirements to evaluate opportunities for the use of reclaimed water under chapter 90.46 RCW. | The King County Water Reclamation Evaluation Checklist is included in Appendix H. |
| (22) | State Environmental Policy Act documentation. | The District completed a State Environmental Policy Act (SEPA) checklist for the Plan and, as lead agency under SEPA, issued a determination of nonsignificance for the approval of the Plan on September 21, 2022. |
| COUNTYWIDE PLANNING POLICIES |
| (23) | FW-4: Support fiscal sustainability for infrastructure and services that serve rural areas. | The wastewater service area does not extend into the rural area of unincorporated King County. The District’s policies state that it will follow King County regulations limiting public sewer expansions in the Rural Area except where needed to address specific health and safety problems threatening the existing uses of structures, or the needs of public schools or public-school facilities. The policy further states sewer service to uses in the Rural Area will be permitted only by “tightline” and only after a finding is made by King County that no reasonable alternative technologies are technologically or economically feasible. |
| (24) | PF-11: Require water reuse and reclamation where feasible. | See #8 above. |
| (25) | DP-3 and PF-3: Coordination of capital facilities and service plans to promote efficient land use and reliable and cost-effective services. | The review by the UTRC and approval by the County Council promotes coordination of capital facilities and service plans. |
| (26) | DP- 14: Adopted infrastructure plans are consistent with adopted growth targets. | The Plan acknowledges the unincorporated King County zoning classifications. This information is used to develop maximum zoning capacity population estimates. The customer information from the end of 2019 forms the basis for population and growth forecasts. Growth rates in the Plan are compiled from: (1) currently proposed developments; (2) Sammamish Town Center assumptions; and (3) conversion of existing homes from septic to sewer service. The Plan notes the Puget Sound Regional Council (PSRC) estimated growth rate for 2020 through 2025 is only 0.59 percent which does not appear to be in line with the known growth in the District. The infrastructure plan for the service area assumes some properties currently served by onsite septic will be connected to sewer system within the planning horizon. |
| (27) | DP-49, PF-1 and PF-13: Limit the extension of urban infrastructure improvements through the Rural Area. | The Plan contains policies that address and acknowledge limitation of sewer service in the rural area. The District follows King County regulations limiting public sewer expansions in the Rural Area and on Natural Resource Lands except where needed to address specific health and safety problems threatening the existing uses of structures, or the needs of public schools or public school facilities. The Plan includes provisions that state sewer service to uses in the Rural Area will be permitted only by “tightline” and only after a finding is made by King County that no reasonable alternative technologies are technologically or economically feasible. |
| (28) | PF-12: With few exceptions, require development with the UGA to be served by public sewer. | See #9 above. |
| KING COUNTY COMPREHENSIVE PLAN POLICIES |
| (29) | F-101 and F04: Forging partnerships in identifying appropriate service providers and coordinate planning efforts. | The review and adoption of the Wastewater Plan demonstrates partnership and coordination efforts. |
| (30) | F-107 and F-209: Plan for provision of services to rural areas. | The Plan includes language that allows for service in the rural area only if it is specifically allowed by King County. |
| (31) | F-201 and F-210: Water and sewer utilities that provide services to unincorporated King County shall prepare capital facility plans consistent with requirements of the GMA and King County Comprehensive Plan. | The General Sewer Plan is consistent with the GMA and King County Comprehensive Plan as it limits service to within the designated urban area and derives the District’s build-out development capacity from the local jurisdictions adopted land use plans/zoning classifications. |
| (32) | F-255: All development within UGA to be served by public sewers, with some exceptions. | See #9. Above. |
| (33) | F-256: King County and sewer utilities should jointly plan for phasing out of on-site systems within UGA. | The Plan references King County requirements for connection to sewer within the urban area if there is a failing onsite septic or a remodel that requires modification to the onsite septic and the property is within 200 ft of the collection system. The Plan further includes an implementation policy for septic conversions that calls for policies and funding mechanisms to support extension of sewer service to areas currently using septic systems. |