#### Major Ongoing Capital Projects 2021-2022

#### Joint Ship Canal Water Quality

The Ship Canal Water Quality Project is a joint project with the City of Seattle. The 2.7-mile tunnel project is mandated through separate consent decrees the County and City have with the EPA and Ecology. The project is expected to prevent an average of 75 million gallons of uncontrolled sewage overflows annually and currently is in construction with an anticipated completion date of 2025.

#### Georgetown Wet Weather Treatment Station

The Georgetown Wet Weather Treatment Station project is also driven by consent decree. It includes the construction of a CSO wet weather treatment station between the Brandon Street and South Michigan Street Regulator Stations; related pipes; and a new outfall structure to release the treated water into the Duwamish River. When constructed, the station will treat up to 70 million gallons a day of combined rainwater and wastewater that would otherwise have discharged directly to the Duwamish without treatment during storm events. This project is expected to finish construction in 2022.

#### West Point Power Quality Improvements

On February 25, 2021, the County Executive transmitted legislation to the County Council and signed a Declaration of Emergency to provide the West Point Treatment Plant with more reliable power in response to increasing power disruptions. The project will either modify on-site power cogeneration at West Point, install a large battery system to help buffer the power supply, or both, which will enable plant equipment to continue operating during power disruptions. This work is expected to be completed by February 28, 2023.

#### North Mercer Island/Enatai Sewer Upgrade

This project will increase the reliability and capacity of the existing North Mercer Island Interceptor and Enatai Interceptor components of the regional wastewater system to convey the 20-year peak wastewater flows projected through the year 2060. Project construction will include approximately 17,210 linear feet of new sewer pipeline and related features and will upgrade the County’s North Mercer Pump Station on Mercer Island. This project is anticipated to start construction in 2021 and extend until 2025.

#### Interbay Sewer and Odor Control Upgrade

The County will upgrade an aging sewer pipe in Seattle’s Interbay neighborhood. The existing pipe was built in 1967 and is nearing the end of its service life. New odor-control technology will be added to the system while the sewer pipe upgrade is underway. When complete, the sewer will provide reliable service for another 50 years or more. Construction is anticipated to be complete by 2024.

A “peak” flow is a sudden and/or sustained increase in the flow.