| Review of the City of Tukwila Comprehensive Sanitary Sewer Plan Update |
| --- |
| Service Area The City of Tukwila owns and operates a municipal sewer system that serves approximately 8.9 square miles in central King County. The City maintains a number of service agreements with neighboring utility districts, cities and King County for the provision of sewer services. The existing land use and zoning within the planning area is designated by two jurisdictions: King County and City of Tukwila. The City’s planning area is bounded by adjacent jurisdictions with which the City has existing service agreements. The service area is not expected to significantly change in the future. The City currently serves approximately 9,059 equivalent residential units (ERUs). One ERU is defined as the average quantity of water beneficially used by one average, full-time, single-family residence per day. The City projects having 22,179 ERUs in 2020 and 29,444 ERU’s in 2030. Approximately two-thirds of the City’s wastewater flow comes from commercial accounts. The City is in the process of updating its franchise with the County. The City’s system consists of approximately 38 miles of collection pipe ranging in size from 8 inch diameter up to 36 inch diameter pipe, ten lift stations, and is divided into 20 drainage basins. The City has 25 connections to King County trunk lines and the majority of wastewater from the City is treated at King County’s South Plant. The City also discharges to the Seattle system and that wastewater is eventually conveyed to the King County system at West Point. The Plan contains a capital improvement plan with an estimated cost of $16.7 million in sewer capital projects for the next six years. Long-term projects are estimated to cost $27.1 million in 2011 dollars. The City has identified funding sources for the proposed improvement projects which include rates, general facilities charges and bond proceeds. The City’s financial plan anticipates sewer and water rate increases of 20 percent in 2014, and 10 to 15 percent increases in 2015 through 2018. Reclaimed Water The City currently receives and uses reclaimed water and is willing to work with King County to identify opportunities and explore additional options to produce and deliver reclaimed water. The City completed the King County Reclaimed Water Checklist. SEPA The City completed a State Environmental Policy Act (SEPA) checklist for the Plan and, as lead agency, issued a determination of non-significance for the issuance of the Plan on January 10, 2014. There were no appeals. |
|  | A. General and sewer plan-specific: King County Code (KCC) 13.24.010 | Comments/findings |
| (1) | The code is applicable to sewer utilities that provide sewer collection or treatment in unincorporated areas of King County and/or are component agencies of the regional wastewater system. | A portion of the City’s service area lies within unincorporated King County. The City is a component agency of the regional wastewater system and so review pursuant to KCC 28.84.050 is also applicable. |
| (2) | Plans should be submitted every six years or sooner if required by the Washington State Department of Ecology whenever sewer conditions have changed significantly within the sewer service area. | The City’s sewer plan was last approved by King County in 2005. |
| (3) | The Plan must meet criteria in Revised Code of Washington (RCW) chapter 90.48 as well as KCC as follows: (1) compliance with the development program and policies outlined in the King County Comprehensive Plan for sewage facilities; and (2) compliance with the basin-wide water and/or sewerage plan. | Yes. See the following for specifics on the various King County Comprehensive Plan policies applicable to wastewater plans and consistency with other planning processes. |
| (4) | The City’s infrastructure for existing and future service areas based on adopted land use map. | Yes, for that portion of the service area in unincorporated King County, the land use and zoning was appropriately used in determining the sewer demand projection. |
| (5) | The Plan contains sufficient information to demonstrate the ability to provide service consistent with the requirements of all applicable statutes, codes, rules, and regulations. | Yes. The City used a new system hydraulic model to evaluate its collection capacity and concluded that there is adequate capacity to accommodate peak flows and anticipated growth to the year 2030 with upgrades to 2 lift stations. |
| (6) | The Plan is consistent with Washington Administrative Code (WAC) 173-240-050. | Yes, the City will seek plan approval from the Department of Ecology. |
| (7) | The Plan discusses the following: Existing and planned flows average and peak; Existing and planned flows for any basin discharging into county system; Amounts of inflow and infiltration (I/I), in comparison with county standard of 1,100 gallons per-acre-per-day (gpad), and steps being taken to reduce; Areas of concern regarding corrosion and odor control and steps being taken; Opportunities for reclaimed water; and Additional information required by the Utilities Technical Review Committee (UTRC). | All are discussed in the Plan: 1, 2, & 3. The existing and planned flow per ERU of 145 gallons per residential ERU is reasonable as is the projection of 120 gallons per commercial ERU. The City worked with the King County Wastewater Treatment Division on the regional I/I control program. Empirical data from the City’s lift station 2 was used to determine an I/I at 1,950 gallons per acre per day (gpad). 4. There were no issues identified with either corrosion or odor control. 5. The City supports King County’s planning efforts regarding reclaimed water opportunities and completed the County’s Reclaimed Water Checklist. 6. In its review of the Plan, the UTRC asked for additional information, which has been provided by the City either in the final Plan or in direct communication with the UTRC. |
|  | B. Public Sewer Service: 13.24.035 |  |
| (8) | The Plan proposes that all developments within Urban Growth Area served by sewer unless on-site are allowed as temporary per KCC 13.24.136 and 13.08.070. | There are unserved areas within the City’s sewer service area and the City has a program to extend service to those areas. |
| (9) | Public sewer is provided in rural towns if approved by King County. | There are no rural towns in the City’s sewer service area. |
| (10) | No public sewer service outside Urban Growth Area unless authorized under KCC 13.24.134. | All of the City’s sewer service area is within the Urban Growth Area. Sewer service is consistent with KCC 13.24.035. |
| (11) | Required elements of sewerage general plan, as called for in RCW 36.94.010(3), are included in King County Comprehensive Plan and Technical Appendix. | Yes, the Plan has the general location and description of treatment and disposal facilities, trunk and interceptor sewers, pumping stations, monitoring and control facilities, local service areas, and preliminary engineering in adequate detail to assure technical feasibility and, to the extent known, the methods of distributing the cost and expense of the system and the economic feasibility of plan implementation. |
|  | C. Consistency requirements: 13.24.060 |  |
| (12) | State and local health requirements. | The Plan has not yet been reviewed and/or approved by the Department of Ecology. The UTRC review process included a representative of Public Health-Seattle and King County. |
| (13) | Elimination or prevention of duplicate facilities. | The City has written agreements with other sewer providers regarding areas to be served in order to avoid overlapping jurisdiction and to ensure efficiency in the use of existing facilities. |
| (14) | Promotion of most healthful and reliable services to the public. | Yes. |
| (15) | Provision of service at a reasonable cost, and maximization of use of public facilities. | Currently the City charges a rate that is in the affordable range. In general, the City collects revenues in excess of expenditures. |
| (16) | Reduction of number of entities providing sewer service in King County. | The City has written agreements with other sewer providers regarding areas to be served in order to avoid overlapping jurisdiction and to ensure efficiency in the use of existing facilities. |
| (17) | Basin wide or multibasin water plans, sewerage plans, or both when approved by the Washington State Department of Ecology or the Washington State Department of Health. | The City is aware of, and supports, the planning done for salmon recovery purposes. The City is part of the regional wastewater system managed by King County. |
| (18) | Applicable state water quality, water conservation (e.g., RCW 90.48.495), and waste management standards. | Yes. As the City implements water conservation programs, there may be a minimal impact on the operation of the sewer system. |
| (19) | Growth Management Act; chapter 36.70A RCW. | Yes, the Plan is consistent with the King County Comprehensive Plan. See specific policies below. |
| (20) | Groundwater Management Plans. | The Plan does reference groundwater protection as one of the goals of the sewer plan. |
| (21) | Federally-approved habitat conservation plans and recovery plans under Endangered Species Act, and other plans, including regional water supply or water resource management plans. | The Plan considers salmon recovery issues as it plans for sewer service. There is no applicable regional water supply plan. |
| (22) | Applicable requirements to evaluate opportunities for the use of reclaimed water under chapter 90.46 RCW. | Yes, the City supports King County’s reclaimed water planning efforts. |
| (23) | Sewer facilities allowed crossing rural areas only under certain conditions and only for schools or public health emergencies, under certain conditions. KCC 13.24.132. | Not applicable. |
| (24) | State Environmental Policy Act documentation. | Yes, the City issued a Determination of Nonsignificance for the plan adoption on January 10, 2014 with no appeals. |
|  | COUNTYWIDE PLANNING POLICIES |  |
| (25) | PF‐10: Encourage water reuse and reclamation, especially for high‐volume non‐potable water users such as parks, schools, and golf courses. | The City will continue to work with King County to identify opportunities and explore additional use of reclaimed water. |
| (26) | PF‐11: Require all development in the Urban Growth Area to be served by a public sewer System with minor exceptions. | Yes, the City is committed to serving the Urban Growth Area. |
| (27) | PF‐12: Prohibit sewer service in the Rural Area and on Resource Lands except: a) where needed to address specific health and safety problems threatening existing structures; or b) as allowed by Countywide Planning Policy DP‐47; or c) as provided in Appendix 5 (March 31, 2012 School Siting Task Force Report). | Not applicable. |
|  | KING COUNTY COMPREHENSIVE PLAN POLICIES |  |
| (28) | F-107: plan for provision of services to rural areas. | Not applicable. |
| (29) | E- 408 King County should carry out conservation planning efforts in close collaboration with other local governments, tribes, state and federal governments, land owners, and other conservation planning stakeholders. | Yes. |
| (30) | E-422: King County’s land use planning, regulatory, and operational functions related to environmental protection, public safety, and equity should be closely coordinated across departments and with other applicable agencies and organizations to achieve an ecosystem-based approach. | Not applicable. |
| (31) | E-434: Habitats for species that have been identified as endangered, threatened, or sensitive by the state or federal government shall not be reduced and should be conserved. | Yes, the City operates the system to protect habitat. |
| (32) | F-108 work with cities and service providers to provide services. | Yes, the City has agreements with neighboring service providers to ensure coordinated service. |
| (33) | F-202: ensure adequate supply of public facilities to support communities. | Yes. The City included review and incorporation of information from the most recent King County Comprehensive Plan. |
| (34) | F-204: work with cities, special purpose utilities, and other service providers to define regional and local services and determine appropriate providers. | Yes. The City has written agreements with local governments and special purpose utilities regarding service provision and coordination with other systems. |
| (35) | F-208: funding for growth should support facilities needed within Urban Growth Areas, prioritized and coordinated through capital improvement programs (CIP), to comply with concurrency requirements. | Funding sources are identified to support identified needs, including facilities to serve anticipated population growth under local comprehensive plans. Extension of the sewer system will be primarily by developer extension agreements. |
| (36) | F-209: support rural levels of development and not facilitate urbanization. | Yes. |
| (37) | F-211: coordinate development of utility facilities. | Yes, see 34. |
| (38) | F-212: King County’s CIP demonstrates that projected needs for facilities and services can be met within the Urban Growth Area in compliance with concurrency requirements; where not possible, identify strategies including phasing and financing. | Yes. The City’s CIP identifies facilities and a funding strategy to ensure that it will meet anticipated demands. |
| (39) | F-214: water and sewer utilities that provide their services to unincorporated King County, shall prepare capital facility plans consistent with requirements of the Growth Management Act and King County Code. | Yes. |
| (40) | F-221: King County shall initiate a subarea planning process with any service provider that declares, through their capital facilities plan, an inability to accommodate projected service needs inside their service area. | Not applicable as the City has the ability to accommodate projected service needs in the service area. |
| (41) | F-223: if an area-wide sewer, water, or transportation deficiency is identified, King County and applicable service providers shall remedy the deficiency through a joint planning process. | Not applicable. |
| (42) | F-255: in the Urban Growth Area, all new development shall be served by public sewers with minor exceptions. | Yes, the City is prepared to serve the urban area. |
| (43) | F- 256: in the Urban Growth Area, King County and sewer utilities should jointly prioritize the replacement of onsite systems that serve existing development with public sewers, based on the risk of potential failure. King County and sewer utilities should analyze public funding options for such conversion and should prepare conversion plans that will enable quick and cost-effective local response to health and pollution problems that may occur when many on-site systems fail in an area. | Yes, the City has policies in place to ensure and encourage the use of the sanitary sewer system within the urban area. Extension of the sewer system will be primarily by developer extension agreements. The City acknowledges that many existing on-site systems exist within its service area and has policies in place to phase out their use over time. |
| (44) | F-259: sewer facilities such as pump stations, force mains and trunk lines that do not provide connections to the rural area may be located in the rural area only when they are identified in a King County-approved comprehensive sewage system plan and upon a finding by King County that it is technically necessary in providing service to the Urban Growth Area. | Yes, the City understands and abides by this policy. |
| (45) | F-260: on-site facilities in rural and natural resource areas shall be designed, constructed, and operated as permanent facilities. | Not applicable. |
| (46) | F- 261: King County should monitor failing on-site systems and analyze options which may include connecting to sewerage systems where consistent with the King County Comprehensive Plan. | There is no significant number of failing on-site systems within the City’s service area of unincorporated King County. |
| (47) | F-262: collective on-site systems may only be used in rural and natural resource areas under specified conditions. | Not applicable. |