## STAFF REPORT

| Agenda Item: | 10 | Name: | Davin Simmons |
| --- | --- | --- | --- |
| Proposed No.: | 2016-0516 | Date: | December 6, 2016 |

SUBJECT

An ordinance approving the Covington Water District Water System Plan May 2016 Final.

SUMMARY

Proposed Ordinance 2016-0516 would approve the Covington Water District Water System. In August 2016, the Utilities Technical Review Committee (UTRC) finalized a review of the Plan and recommended approval. The purpose of this Plan is to develop a long-term planning strategy for the District’s water service area.

BACKGROUND

The Covington Water System Plan has been developed in accordance with Chapter 246-290 of the Washington Administrative Code (WAC), as an update to the 2007 Plan. The Plan evaluates over a 20 year period its abilities to meet the following anticipated requirements:

Water source, quality, transmission, storage and distribution

Planning level costs of improvement projects

Financial Plan for funding of projects

UTRCS ANALYSIS OF COVINGTON WATER DISTRICT WATER SYSTEM PLAN

The UTRC has finalized its review of the Plan on August 17, 2016. The UTRC found the Plan meets the requirements of KCC chapter 13.24 and has recommended its approval. Highlights of the Plan, as reviewed by the UTRC, are outlined below.

Service Area: The District’s service is approximately 55 square miles and serves all of the City of Covington and potions of the Maple Valley and Black Diamond, along with areas of unincorporated King County. The District serves a population of approximately 50,000 through 17,031 water connections as of the end of 2013.

Facilities: Then District’s water system is a multi-source that supply, treatment, storage and distribution of potable water to residential, governmental/educational and irrigation customers with water sources. This includes 12 groundwater wells and the Green River Regional Water Supply System (RWSS). The District has approximately 289 miles of pipeline, three interties with the RWSS (with plans for a fourth), six online booster pump stations, eight reservoirs, four interties with the Cedar River Water and Sewer District, one emergency intertie with King County Water District 111 and an emergency intertie with Auburn. The District receives approximately 80 percent of its supply from the RWSS and the remaining 20 percent from its wells.

Growth: The District’s existing sources are expected to accommodate growth beyond 2060.

System Improvements: A number of improvements to the existing water supplies are recommended to increase reliability, interties and water quality improvement. The planned RWSS interties should be constructed to improve system hydraulics and operational flexibility. The District has an ongoing and effective Water Use Efficiency program. However, to support growth in its Sugarloaf satellite facility a second well, Well #4, is being developed.

SEPA: The District completed a State Environmental Policy Act (SEPA) checklist for the Plan and as lead agency under SEAP, issued a determination of non-significance for the Plan on September 16, 2015. There were no appeals.

ATTACHMENTS

- Proposed Ordinance 2016-0516 (with attachments)

- UTRC Review of the City of Covington Comprehensive Water Plan

- Transmittal Letter dated October 7, 2016