| Review of the Ames Lake Water Association Water System Plan, September 2018 |
| --- |
| Service Area The Ames Lake Water Association (ALWA) is an association that owns and operates a Class A water system. The ALWA is located in unincorporated King County north of the community of Fall City, and west across the Snoqualmie River from the City of Carnation. Its water system provides service to an area of approximately ten square miles, and primarily covers the upland areas known as Tolt Hill. The water service area for ALWA is bordered by the City of Carnation water system, Sammamish Plateau Water, Camp Korey (former Nestle Regional Training Center), and the Fall City Water District. The ALWA has no plans to expand its service area in the future. The ALWA holds franchise number 11921 for water distribution; the franchise is current and expires on August 7, 2020. Water Use Efficiency In 2016, the ALWA’s water system provided service to a population of approximately 3,104 residents through 1,107 active residential connections. The ALWA currently serves two customer classes, residential and commercial. The ALWA also serves two commercial connections, a small tree nursery and the Nestle Regional Training Center (formerly Carnation Farms laboratory facility). Both of the commercial customers' water use is within the range of the ALWA's residential customers; therefore, for planning purposes, these commercial customers are projected to have usage similar to that of the ALWA's residential customers. The total number of connections has increased by less than one percent from 2008 to 2016. Average daily water demand is approximately 181,700 gallons per day (gpd). The ALWA uses a peaking factor of 2.16. The ALWA currently has an average equivalent residential unit use of 152 gpd. The 2016 annual average distribution system loss is approximately 4.7 percent, with a three-year average value of 3.7 percent, which is less than the statutory standard of ten percent. The major components of the ALWA's water system include eight groundwater wells, two treatment facilities, six reservoirs and three booster stations to serve seven pressure zones through nearly 39 miles of pipeline. The ALWA owns eight wells with an ability to produce approximately 397.32 acre-feet per year of water. The ALWA currently has an intertie with Sammamish Plateau Water. The Plan contains a ten-year capital improvement program (CIP) with an estimated cost of approximately $2.5 million dollars. Two booster station projects and four distribution system projects are identified in the CIP. The funding sources for the proposed improvement projects include rates and water service fees. Reclaimed Water The ALWA completed King County's Reclaimed Water Checklist and, while recognizing the value of reclaimed water, does not currently use any reclaimed water. SEPA The ALWA completed a State Environmental Policy Act (SEPA) checklist for the Plan and, King County, as lead agency, issued a determination of nonsignificance for the issuance of the Plan on October 25, 2018. There were no appeals. |
| A review of the specific statutes, rules, codes and policies to the water system plan is as follows: |
|  | A. General water plan, King County Code (KCC) 13.24.010 and 13.28 | Comments/findings |
| (1) | Review is applicable to water utilities distributing or obtaining water in unincorporated King County, and/or utilities that distribute water within a Critical Water Supply Service Area (Ch. 70.116 RCW). Is there a need to meet the consistency requirements of RCW 43.20.260? | Yes, the Ames Lake Water Association's (ALWA) comprehensive water plan (Plan) is subject to King County Council approval under Ch. 70.116 RCW and King County Code (KCC). The ALWA provides water service to a part of eastern unincorporated King County. Yes, the ALWA also needs to demonstrate consistency for its Plan under RCW 43.20.260. |
| (2) | Consistency with King County Comprehensive Plan (KCCP) and development regulations, and policies including KCC 21A.28.040 development standards, provision of adequate supplies for anticipated growth and development. | Yes, the ALWA's Plan is consistent. |
| (3) | Infrastructure for existing and future service areas based on adopted land use map. | Yes. The ALWA's service area is located entirely in unincorporated King County. The King County land use map is used in the Plan |
| (4) | Review proposals for modified or expanded service areas based on compliance with utility's approved plan, and ability to meet duty to serve requirement. | Not applicable. The ALWA's service area is well defined and is bounded on several sides by other water utilities. The service area has not changed recently, and the ALWA does not expect it to change. |
| (5) | Sufficient information to demonstrate the ability to provide service consistent with the requirements of all applicable statutes, codes, rules, and regulations. | Yes, the Plan demonstrates the ALWA's ability to provide service consistent with applicable statutes, codes and regulations. The ALWA obtains its water from eight wells located in two well fields. The projected daily demand in 2036 is 210,700 gallons per day (gpd). The current annual water rights are projected to meet the ALWA's demands through the 20-year period. |
| (6) | Monitor and review effectiveness of purveyor conservation plans if within area covered by an approved Coordinated Water System Plan (CWSP). | The ALWA is in the area covered by the East King CWSP. Through its membership in the East King County Regional Water Association the ALWA participates in the Partnership for Water Conservation. The ALWA's water use efficiency plan is organized to conform to the requirements of the Water Use Efficiency Rule. |
|  | B. Consistency requirements: 13.24.060 |  |
| (7) | State and local health requirements. | Yes. |
| (8) | Creation and maintenance of logical service areas. | Yes, the service area is logical. |
| (9) | Elimination or prevention of duplicate facilities. | The ALWA's boundaries are well fixed and not expected to change, with other utilities abutting the ALWA on several sides. |
| (10) | Promotion of most healthful and reliable services to the public. | Yes. Water purveyed by the Association complies with public health standards. A hydraulic analysis performed indicates that the ALWA has significant storage deficiencies within the 592 Zone and zones supplied by it. The Tolt Hill Booster Pump Station is undersized and lacks auxiliary power supplies. There is insufficient pressure in the distribution system in the Ridgehaven area. Under current conditions, fore flow is not provided at 1,00 gpm anywhere in the system. The ALWA's CIP addresses each of these needs. |
| (11) | Provision of service at a reasonable cost, and maximization of use of public facilities. | Yes, the ALWA's rates for water service are comparable to the rates charged by similar utilities. The ALWA's current rate schedule was adopted in 2008. The ALWA has adopted a graduated rate structure to encourage efficiency of water use. |
| (12) | Basin-wide or multi-basin water plans, sewerage plans, or both when approved by the Washington State Department of Ecology (Ecology) or Department of Health (DOH). | The ALWA has not been involved in multi-basin water plans, although it is an associate member of the East King County Regional Water Association. The ALWA neither collects nor treats wastewater. |
| (13) | Applicable state water quality, water conservation, and waste management standards. | The ALWA's water meets applicable water quality standards. The ALWA's water use per equivalent residential unit (ERU) in 2006 was 145 gpd, not accounting for distribution system losses. The ALWA is calculating maximum day demand at 2.16 times average day demand. The three-year rolling average distribution system leakage is estimated at 3.7 percent, which is less than the ten percent requirement established under the Municipal Water Law. |
| (14) | Water Resources Act (RCW 90.54). | The ALWA has had a conservation program in place since 1990. The Association's Water Use Efficiency Plan is organized to conform to the requirements of the Water Use Efficiency Rule adopted by DOH. The Plan makes no connection between the Association's conservation program and the requirements of RCWs 90.54.180 and 90.03.386 |
| (15) | Growth Management Act (GMA) (RCW 36.70A). | The ALWA appropriately used King County land use zoning for its entire service area. The ALWA used Puget Sound Regional Council (PSRC) data in preparing its population forecasts. |
| (16) | Groundwater management plans. | The ALWA has a Well Head Protection Program for the groundwater sources. |
| (17) | Federally approved habitat conservation plans and recovery plans under the Endangered Species Act (ESA). | Not discussed in Plan. |
| (18) | Requirements for salmon recovery under Ch. 77.85 RCW, and other plans, including regional water supply or water resource management plans. | Not discussed in Plan. |
|  | C: Countywide Planning Policies |  |
| (19) | G-4: Adopt comprehensive plans that are consistent with the Countywide Planning Policies as required by the Growth Management Act. | Yes. |
| (20) | EN-19: Promote energy efficiency, conservation methods and sustainable energy sources to support climate change reduction goals. | Not discussed in Plan. |
| (21) | DP-13: All jurisdictions shall plan to accommodate housing and employment targets. This includes coordinating water, sewer, transportation and other infrastructure plans and investments among agencies, including special purpose districts. | The ALWA's service area is located entirely within unincorporated King County. Future water service population is based on PSRC data for King County. |
| (22) | PF-2: Coordinate among jurisdictions and service providers to provide reliable and cost-effective services to the public. | The ALWA is a member of the East King County Regional Water Association, which develops the East King County Coordinated Water System Plan (CWSP). The East King County CWSP develops a regional approach to coordinating water service boundaries and presents an assessment of the future water supply in the region. |
| (23) | PF-4: Develop plans for long‐term water provision to support growth and to address the potential impacts of climate change on regional water resources. | Sufficient water supply for near-term growth is available. Climate change is not mentioned. |
| (24) | PF-7: Plan and locate water systems in the Rural Area that are appropriate for rural uses and densities and do not increase the development potential of the Rural Area. | The ALWA's service area is located entirely within rural unincorporated King County. Future water service needs are based on PSRC data for King County. |
| (25) | PF-8: Recognize and support agreements with water purveyors in adjacent cities and counties to promote effective conveyance of water supplies and to secure adequate supplies for emergencies. | The ALWA is self-supplied from eight wells. The ALWA is located within the East King County Critical Water Supply Service Area, and its Plan is subject to consistency with the East King County CWSP. |
| (26) | PF-9: Implement water conservation and efficiency efforts to protect natural resources, reduce environmental impacts, and support a sustainable long‐term water supply to serve the growing population. | The water conservation and efficiency efforts of the ALWA meet the minimum required by statute. |
| (27) | PF-10: Encourage water reuse and reclamation, especially for high‐volume non‐potable water users such as parks, schools, and golf courses. | The ALWA evaluated water reclamation opportunities and found utilization of reclaimed water to not be viable at this time. The ALWA's service area is currently 100 percent served by in-ground wastewater treatment (septic) systems, with no reclaimed water distribution lines within its service area. |
|  | D: King County Comprehensive Plan (KCCP) |  |
| (28) | F-107: With special purpose districts or local service providers, plan for provision of services to rural areas. | Yes, since the ALWA's service area is entirely within rural unincorporated King County. |
| (29) | F-108: King County to work with cities and service providers to establish priority areas for public funding of capital facilities. | Yes, King County will do this. |
| (30) | F-201: All facilities and services should be provided in compliance with provisions and requirements of the Endangered Species Act and the Clean Water Act. | Yes. |
| (31) | F-209: In the Rural Area, services provided by agencies should support a rural level of development and not facilitate urbanization. | The ALWA uses County zoning and PRSC data for planning future service area needs. |
| (32) | F-210: capital facility plans and capital improvement programs for services to unincorporated King County are consistent with the KCCP. | Yes, the ALWA's capital facility plans and capital improvement programs for services to unincorporated King County are consistent with the KCCP. |
| (33) | F-211: King County helps coordinate development of utility facilities with other projects that utilize public rights-of-way and easements, where possible. | Yes, this is done. |
| (34) | F-221: King County shall initiate a sub-area planning process with any service provider that declares, in its capital facilities plan, an inability to meet service needs within service area. | Not applicable as the ALWA did not identify an inability to meet service needs within its service area. |
| (35) | F-223: If a service deficiency is identified in a service provider's existing service area, King County and the applicable service provider shall remedy the deficiency through a joint planning process addressing capital improvement programs and long-term funding strategies. | Not applicable as the ALWA did not identify an inability to meet service needs within its service area. |
| (36) | F-231: King County supports coordination of regional water supply planning, sales of excess water supplies among municipalities in the region, water quality programs and water conservation, reuse and reclaimed water programs. | The ALWA has an intertie with the Sammamish Plateau Water and Sewer District, which was completed in 2012, to provide emergency water supply. |
| (37) | F-232: Water utilities that obtain water from, or distribute water in unincorporated King County, and water utilities formed as special purpose districts under Title 57 RCW are required to submit water system plans to the county for review and approval and shall describe in their plans how they intend to meet their duty to provide service within their retail service area. | Yes, the ALWA’s entire service area is located in unincorporated King County, and the Plan describes how it intends to meet its duty to provide service within its retail service area. |
| (38) | F-246: King County supports interties that allow the transfer of water resources among water utilities to meet the projected demands for growth where such interties meet the requirements of RCW 90.03.383 and are also consistent with any applicable locally adopted comprehensive plans, regional water supply plans, adopted groundwater management plans, watershed plans, approved Coordinated Water System Plans, Endangered Species Act response requirements and Clean Water Act requirements. | The ALWA has an intertie with the Sammamish Plateau Water and Sewer District, which was completed in 2012, to provide emergency water supply. |
| (39) | F-249: Utilities with more than one thousand service connections required to submit water system plans for approval to King County shall include an evaluation of reclaimed water use opportunities by completing King County's Water Reclamation Evaluation Checklist. | Yes, the ALWA completed King County's Water Reclamation Evaluation Checklist. |
| (40) | F-251: In its review of water system plans, the UTRC shall consider the criteria provided in K.C.C. 13.24.010, 13.24.060, and 13.24.070, and determine the plan's consistency with the following: a. Applicable provisions of the King County Comprehensive Plan, land use plans, and development regulations adopted under the Growth Management Act; b. Approved or adopted regional water resource plans, such as basin plans, groundwater plans, watershed-based conservation and recovery plans developed under ESA, salmon recovery plans developed under chapter 77.85 RCW, water resource plans developed under chapter 90.54 RCW, watershed plans developed under chapter 90.82 RCW, and a regional water supply plan or water resource management plan; c. The county's Regional Wastewater Services Plan; and d. Other applicable provisions of countywide plans managed by King County, as specified in UTRC guidance or checklists. | The UTRC has reviewed the planning data and ALWA's operations and has found the plan is consistent with: a. the King County Comprehensive Plan, land use plans and development regulations; b. to the extent applicable, the basin plans, groundwater plans, watershed-based conservation and recovery plans for the service area; and c. other applicable provisions. |
| (41) | F-252: In reviewing proposals for modified and expanded service area boundaries for municipal water suppliers, the UTRC shall consider, in addition to Policy F-251: a. Compliance by the water system with its water system comprehensive plan, including water conservation elements; b. Whether it can meet its duty to provide service within its service area, as required under chapter 43.20 RCW; and c. Consistency with the service provisions of any applicable Coordinated Water System Plan, as adopted in King County Code Chapter 13.28. | Not applicable as the ALWA is not changing its water service area. |
| (42) | F-253: Consistent with Countywide Planning Policies, public drinking water system surface water reservoirs and their watersheds should be managed primarily for the protection of drinking water, but should allow for multiple uses, including recreation, when such uses do not jeopardize drinking water quality standards. Public watersheds must be managed to protect downstream fish and agriculture resources. | Not applicable. |
| (43) | F-254: Groundwater-based public water supplies should be protected by preventing land uses that may adversely affect groundwater quality or quantity to the extent that the supply might be jeopardized. The county shall protect the quality and quantity of groundwater used as water supplies through implementation of Policies E-493 through E-497 where applicable. | Yes, this is accomplished through the Well Head Protection Program and the critical areas ordinances. |