| Review of the King County Water District 54 Comprehensive Water System Plan, October 2019 |
| --- |
| Service Area King County Water District 54’s (District) service area extends from South 212th Street on the north to the Kent Des Moines Road on the south and from Puget Sound on the west to 14th Avenue on the east. The retail service area is an area of approximately 0.7 square miles and encompasses parts of the City of Des Moines and the City of Normandy Park. The service area is nearly fully developed. As of 2019, the district served a population of approximately 5,200 through 755 water service connections. The water service connections equate to approximately 2,205 equivalent residential units (ERU). Production of water per ERU averaged 160 gallons per day for the time period 2012 through 2017, a reduction of 12% from the last planning period. The service area is surrounded by the Highline Water District service area and is not expected to change in the future. The district does not hold a franchise with the County given there are no unincorporated areas within its service area. Water Use Efficiency The district obtains its water from four groundwater wells. Additionally, the district maintains an emergency water system intertie with the Highline Water District. With conservation, average per capita water use was 67 gallons per day in 2017. The average peaking factor is 1.87 which is the ratio of average day demand to peak day demand. A peaking factor of 2.10 is used to project future water use. The annual distribution system loss rate (how much water the system loses in distribution) has varied from 2.2 percent to 6.6 percent in the past few years. The three-year rolling average distribution system loss is 4.1 percent, which meets the State statutory goal of 10 percent or less. These numbers have dropped from the high double digits following a meter replacement program by the District. The Plan contains a ten-year capital improvement plan with an estimated cost of approximately $3.26 million, and a twenty-year plan costing $6.7 million. The district identified three funding sources for the proposed improvement projects: developer extensions, rates, and general facility charges. Total water operating revenues for the district in 2018 were estimated to be $1,000,438 and same year operating expenses were estimated to be $785,848. Reclaimed Water and Regional Planning The district recognizes the value of reclaimed water as a means to conserve and extend the useful life of the potable water supply. The district worked with King County in the development of the regional reclaimed water planning process and has committed to working with its customers and the County as appropriate to assess the feasibility of using reclaimed water for various non-potable water needs. SEPA The district completed a State Environmental Policy Act checklist and delegated lead agency status to the City of Des Moines. The city issued a Determination of Nonsignificance for the issuance of the plan on December 23, 2019; there were no appeals. |
| A review of the specific statutes, rules, codes and policies to the water system plan is as follows: |
|  | A. General water plan, King County Code (KCC) 13.24.010 and 13.28 | Comments/findings |
| (1) | Review is applicable to water utilities distributing or obtaining water in unincorporated King County, and/or utilities that are special purpose district created pursuant to Title 57 Revised Code of Washington (RCW). Is there a need to meet the consistency requirements of RCW 43.20.260? | Yes, the District's Water System Plan (Plan) is subject to King County Council approval under Title 57 RCW. Yes, The Washington State Department of Health (DOH) also needs to demonstrate consistency for the Plan under RCW 43.20.260. |
| (2) | Consistency with King County Comprehensive Plan (KCCP) and development regulations, and policies including KCC 21A.28.040 development standards, provision of adequate supplies for anticipated growth and development. | Yes, the District's Plan is consistent. |
| (3) | Infrastructure for existing and future service areas based on adopted land use map. | Yes, the district used adopted land use maps. The service area is in the City of Des Moines and City of Normandy Park with no service in unincorporated King County. |
| (4) | Review proposals for modified or expanded service areas based on compliance with utility's approved plan, and ability to meet duty to serve requirement. | Not applicable. The District's service area is well defined and bounded on three sides by other water utilities. The service area has not changed recently and is not expected to change. The district maintains duty to serve policies for its retail service area. |
| (5) | Sufficient information to demonstrate the ability to provide service consistent with the requirements of all applicable statutes, codes, rules, and regulations. | Yes, the Plan demonstrates an ability to provide service consistent with applicable statutes, codes, rules and regulations. The district obtains its water from groundwater sources. The maximum projected daily demand for 2039 is approximately 0.81 million gallons per day (mgd). Average per capita water use was measured at 67 gallons per day in 2017 and is estimated at 66 gallons per day in 2039. The district’s water supplies appear sufficient to meet projected peak day demand in 2039. |
| (6) | Monitor and review effectiveness of purveyor conservation plans if within area covered by an approved Coordinated Water System Plan (CWSP). | The district is within the South King County CWSP. The district’s water use efficiency plan identifies conservation activities which the district employs as part of its long-range conservation plan. KCC 13.28 relates to the CWSP and conservation goals. The District’s conservation measures include a distribution system loss monitoring program, customer education, a seasonal rate adjustment, and meter replacement program. |
|  | B. Consistency requirements: 13.24.060 |  |
| (7) | State and local health requirements. | Yes, water purveyed meets State and local health requirements per reporting in the SENTRY system. |
| (8) | Creation and maintenance of logical service areas. | Yes, the service area is logical. |
| (9) | Elimination or prevention of duplicate facilities. | Yes. The District intends to provide service within its service area by means of direct connection. The District does not foresee any need to provide satellite management services, since direct service is available throughout its service area. The district maintains emergency water system interties with the Highline Water District and mutual aid agreements with King County Water District 125 and Lakehaven Utility District. |
| (10) | Promotion of most healthful and reliable services to the public. | Yes. Water purveyed by the district complies with DOH requirements. The water is neither chlorinated nor fluoridated. District sampling has shown manganese to be present at levels that presents aesthetic concerns rather than health concerns. The district’s response for manganese will depend on acceptability of the water to customers. The existing combination of water sources provides sufficient capacity to meet the requirements of the district through 2039. |
| (11) | Provision of service at a reasonable cost, and maximization of use of public facilities. | Cost of service is comparable to other water districts in the region. |
| (12) | King County Comprehensive Plan and other pertinent county adopted plans and policies. | Yes, there is consistency between the District's Plan and the King County Comprehensive Plan. |
| (13) | Basin-wide or multi-basin water plans, sewerage plans, or both when approved by the Washington State Department of Ecology (Ecology) or Department of Health (DOH). | The District has not been involved in multi-basin water plans, although it does take part in Seattle Public Utility’s (SPU’s) initiatives. The district neither collects nor treats wastewater. The Plan is consistent with the South King County CWSP. |
| (14) | Applicable state water quality, water conservation, and waste management standards. | Yes, applicable standards are met. The District contracts with SPU which conducts the laboratory testing. The District performs coliform monitoring in keeping with State guidelines. The District's distribution system loss (non-revenue or unaccounted-for water) for 2018 was three percent and the three-year average is 4.1 percent and meets the statutory goal. |
| (15) | Water Resources Act (RCW 90.54). | The district will maintain its existing conservation (efficiency) program while complying with DOH’s Water Use Efficiency Rule. |
| (16) | Growth Management Act (GMA) (RCW 36.70A). | The district received consistency statements from the Cities of Des Moines and Normandy Park affirming that the district used planning assumptions and data consistent with adopted city policies. |
| (17) | Groundwater management plans. | The district owns four groundwater wells. Wellhead protection areas for sources have been developed. |
| (18) | Federally approved habitat conservation plans and recovery plans under the Endangered Species Act (ESA). | The Water District does not have surface water usage or discharge which might affect sensitive species or recovery plans. |
|  | Requirements for salmon recovery under Ch. 77.85 RCW, and other plans, including regional water supply or water resource management plans. | The Water District does not have surface water usage or discharge which might affect sensitive species or recovery plans. |
| (19) | C: Countywide Planning Policies |  |
| (20) | G-4: Adopt comprehensive plans that are consistent with the Countywide Planning Policies as required by the Growth Management Act. | Yes, the District adopted a plan that is consistent with Countywide Planning Policies. |
| (21) | EN-19: Promote energy efficiency, conservation methods and sustainable energy sources to support climate change reduction goals. | Not discussed in Plan. |
| (22) | DP-13: All jurisdictions shall plan to accommodate housing and employment targets. This includes coordinating water, sewer, transportation and other infrastructure plans and investments among agencies, including special purpose districts. | Yes, the District asserts it can accommodate population and employment targets of the cities within its service area. |
| (23) | PF-2: Coordinate among jurisdictions and service providers to provide reliable and cost-effective services to the public. | Yes, the District has coordinated with the Highline Water District for emergency water supply. |
| (24) | PF-4: Develop plans for long‐term water provision to support growth and to address the potential impacts of climate change on regional water resources. | The increased water usage associated with population growth within the district can be met using existing water rights and historic production levels. |
| (25) | PF-7: Plan and locate water systems in the Rural Area that are appropriate for rural uses and densities and do not increase the development potential of the Rural Area. | The district’s service area does not include any rural area. |
| (26) | PF-8: Recognize and support agreements with water purveyors in adjacent cities and counties to promote effective conveyance of water supplies and to secure adequate supplies for emergencies. | Yes, the District has an agreement with a neighboring water system with interties for emergency water supply. |
| (27) | PF-9: Implement water conservation and efficiency efforts to protect natural resources, reduce environmental impacts, and support a sustainable long‐term water supply to serve the growing population. | The water conservation and efficiency efforts of the District meet the minimum required by statute WAC 246-290. The distribution system loss in 2017 was three percent with a three-year rolling average of 4.1 percent. The distribution system loss is within or meets State standards of 10% WAC 246-290. |
|  | PF-10: Encourage water reuse and reclamation, especially for high‐volume non‐potable water users such as parks, schools, and golf courses. | The plan does not consider reclaimed water use, as the utility does not have reclaimed water infrastructure or a source. However, the utility has committed to working with its customers and the County as appropriate to assess the feasibility of using reclaimed water for various non-potable water needs |
| (28) | D: King County Comprehensive Plan (KCCP) |  |
| (29) | F-107: With special purpose districts or local service providers, plan for provision of services to rural areas. | The district’s service area does not include any rural area. |
| (30) | F-108: King County to work with cities and service providers to establish priority areas for public funding of capital facilities. | Yes, King County will continue do this. |
| (31) | F-201: All facilities and services should be provided in compliance with provisions and requirements of the Endangered Species Act and the Clean Water Act. | The district’s provision of water service doesn’t rely on impaired waters or habitat; the district meets the Clean Water Act through its compliance with DoH regulations. |
| (32) | F-209: In the Rural Area, services provided by agencies should support a rural level of development and not facilitate urbanization. | The district’s service area does not include any rural area. |
| (33) | F-210: capital facility plans and capital improvement programs for services to unincorporated King County are consistent with the KCCP. | Yes, the District's Capital Improvement Plan is consistent with the KCCP and future land use. |
| (34) | F-211: King County helps coordinate development of utility facilities with other projects that utilize public rights-of-way and easements, where possible. | Not applicable, as the district’s activities occur within city rights-of-way. |
| (35) | F-221: King County shall initiate a sub-area planning process with any service provider that declares, in its capital facilities plan, an inability to meet service needs within service area. | Not applicable as the District did not identify an inability to meet service needs within its service area. |
| (36) | F-223: If a service deficiency is identified in a service provider's existing service area, King County and the applicable service provider shall remedy the deficiency through a joint planning process addressing capital improvement programs and long-term funding strategies. | Not applicable as the District did not identify an inability to meet service needs within its service area. |
| (37) | F-231: King County supports coordination of regional water supply planning, sales of excess water supplies among municipalities in the region, water quality programs and water conservation, reuse and reclaimed water programs. | The District has interties with neighboring utilities to provide emergency water supply; the neighboring Highline Water District obtains -some of its water from SPU. |
| (38) | F-232: Water utilities that obtain water from, or distribute water in unincorporated King County, and water utilities formed as special purpose districts under Title 57 RCW are required to submit water system plans to the county for review and approval and shall describe in their plans how they intend to meet their duty to provide service within their retail service area. | The District does not provide water to unincorporated areas. The District is a special purpose district formed under Title 57 RCW. The District can meet its duty to serve in the designated retail service area. |
| (39) | F-246: King County supports interties that allow the transfer of water resources among water utilities to meet the projected demands for growth where such interties meet the requirements of RCW 90.03.383 and are also consistent with any applicable locally adopted comprehensive plans, regional water supply plans, adopted groundwater management plans, watershed plans, approved Coordinated Water System Plans, Endangered Species Act response requirements and Clean Water Act requirements. | The District has an intertie with the neighboring water utility to provide emergency water supply. |
| (40) | F-249: Utilities with more than one thousand service connections required to submit water system plans for approval to King County shall include an evaluation of reclaimed water use opportunities by completing King County's Water Reclamation Evaluation Checklist. | The Cities of Des Moines and Normandy Park, as lead agencies, did not find opportunities for reclaimed water use. |
| (41) | F-251: In its review of water system plans, the UTRC shall consider the criteria provided in K.C.C. 13.24.010, 13.24.060, and 13.24.070, and determine the plan's consistency with the following: a. Applicable provisions of the King County Comprehensive Plan, land use plans, and development regulations adopted under the Growth Management Act; b. Approved or adopted regional water resource plans, such as basin plans, groundwater plans, watershed-based conservation and recovery plans developed under ESA, salmon recovery plans developed under chapter 77.85 RCW, water resource plans developed under chapter 90.54 RCW, watershed plans developed under chapter 90.82 RCW, and a regional water supply plan or water resource management plan; c. The county's Regional Wastewater Services Plan; and d. Other applicable provisions of countywide plans managed by King County, as specified in UTRC guidance or checklists. | The UTRC has reviewed the planning data and the District's operations and has found the Plan is consistent with: a. the King County Comprehensive Plan, land use plans and development regulations; b. to the extent applicable, the basin plans, groundwater plans, watershed-based conservation and recovery plans for the service area; and c. other applicable provisions. |
| (42) | F-252: In reviewing proposals for modified and expanded service area boundaries for municipal water suppliers, the UTRC shall consider, in addition to Policy F-251: a. Compliance by the water system with its water system comprehensive plan, including water conservation elements; b. Whether it can meet its duty to provide service within its service area, as required under chapter 43.20 RCW; and c. Consistency with the service provisions of any applicable Coordinated Water System Plan, as adopted in King County Code Chapter 13.28. | Not applicable as the District is not changing its water service area. |
| (43) | F-253: Consistent with Countywide Planning Policies, public drinking water system surface water reservoirs and their watersheds should be managed primarily for the protection of drinking water, but should allow for multiple uses, including recreation, when such uses do not jeopardize drinking water quality standards. Public watersheds must be managed to protect downstream fish and agriculture resources. | Not applicable as the District does not control any surface water reservoirs or watersheds. |
| (44) | F-254: Groundwater-based public water supplies should be protected by preventing land uses that may adversely affect groundwater quality or quantity to the extent that the supply might be jeopardized. The county shall protect the quality and quantity of groundwater used as water supplies through implementation of Policies E-493 through E-497 where applicable. | Not applicable at this time as the District's source of water is surface water. The District has a Well Head Protection Program. |